## Slide 1: Volt Compiler Pipeline
Shinnung Jeong
Georgia Tech
MICRO Vortex Tutorial 2026

## Slide 2: Program Execution on the Vortex GPU
Vortex GPU
Kernel binary using the Vortex GPU ISA
Host executable using the Vortex driver
Program
Kernel code with control flow & special func
Host code with device communication
__kernel void foo(){
tid = get_global_id(0);
…
barrier(…);
}
__host int main(){
…
cl_mem A_clmem = clCreateBuffer(context, …); clEnqueueNDRangeKernel(command_queue, …); …
}

## Slide 3: Expanding GPU Variants on Vortex
Vortex GPU Variant
Kernel binary using the Extended Vortex GPU ISA
Host executable using the Extended Vortex driver
__kernel void foo(){
tid = get_global_id(0);
…
barrier(…);
}
__host int main(){
…
cl_mem A_clmem = clCreateBuffer(context, …); clEnqueueNDRangeKernel(command_queue, …); …
}
Program
Kernel code with control flow & special func
Host Code with device communication
HW-Side Consideration
Flexible Hardware & Microarchitecture & Number of HW Component
Flexible ISA & Runtime
SkyBox
SparseWeaver
Tensor Core
Tapeout
Vortex 3.0

## Slide 4: Programs from Diverse Frontends
Program with Diverse Frontends
Kernel code with Frontend-specific semantics
Host Code with Frontend-specific runtimes
HW-Side Consideration
Flexible Hardware & Microarchitecture & Number of HW Component
Flexible ISA & Runtime
Triton
Vortex GPU Variant
Kernel binary using the Extended Vortex GPU ISA
Host executable using Extended Vortex driver
SkyBox
SparseWeaver
Tensor Core
Tapeout
Vortex 3.0

## Slide 5: Key Challenges in Designing VOLT
Challenge 1: Make SIMT-aware code generation and optimizations portable
  How can we preserve SIMT-aware code generation and optimizations while remaining portable across Vortex variants and potentially other open GPUs?
Challenge 2: Support multiple frontends with minimal maintenance overhead
  How can we design the compiler so that new frontends and GPU variants can be added with minimal refactoring?

## Slide 6: Vortex-Optimized Lightweight Toolchain (VOLT)
Front-end Compilers
Middle-end Compiler
Hierarchical Compiler Design
CuPBoP
Back-end Compiler
Design Choice 1
  Hierarchical compiler design
  Centralize fundamental SIMT-related analyses and optimizations in the middle-end
Design Choice 2
  Leverage existing open-source components as much as possible

## Slide 7: Front-end Compiler
Front-end Compiler
CuPBoP
GPU Host Code
Host Code Compilation
Host Runtime for HW Target Translator
Runtime Lib Linking
Semantic Analyzer
Host Binary
Handles both host and kernel code
Host Code
  Compiled for the host hardware
  Translates frontend-specific host functions using the target runtime library
Blue boxes indicate components extended or implemented for the Vortex GPU

## Slide 8: Front-end Compiler
Handles Both Host and Kernel Code
Kernel Code
  Performs semantics-aware code optimizations
  Transforms special functions using built-in libraries
  Inserts thread scheduling and spawning code for device initialization
Front-end Compiler
Semantic-aware Code Optimization
Built-in library
CuPBoP
Built-in Library Linking
Memory Structure Handling
Function Call Analysis
Thread Scheduling Code Generation
Thread Scheduling and Spawn Code Insertion
IR Generator
GPU Kernel Code
LLVM module
Blue boxes indicate components extended or implemented for the Vortex GPU

## Slide 9: Middle-end Compiler
Target-independent optimizations
Minimal target-specific logic
Treats thread divergence management as a first-class concern
  Uniformity Analysis
  Divergence Optimization
LLVM module
Middle-end Compiler
Divergence Management
Optimization and Transformation
Uniformity Analysis
Divergence Management Function Insertion
General Code Optimizations
Divergence Tracker
LLVM module
Blue boxes indicate components extended or implemented for the Vortex GPU

## Slide 10: Middle-end Compiler
Uniformity Analysis
  Divergence Tracker
    Find divergent instructions and always uniform instructions
    Marks function arguments, return values, and atomic operations as divergent
    Marks control and status register information as uniform
    Propagates uniformity information
  Annotation Analysis
    Identifies divergent and always-uniform instructions
    Leverage annotation information from the user or the front-end compiler
  Function Argument Analysis
    Determine the uniformity of each function’s arguments

## Slide 11: Middle-end Compiler
Divergence Optimization
  Code Simplification
    Simplifies and canonicalizes control flow for subsequent divergence handling
  Control-Flow Structurization
    Transforms the CFG into a structured form to provide stable join points
    Essential for IPDOM-based divergence and reconvergence handling
  Control-Flow Reconstruction
    Selectively duplicates basic blocks to reduce predicate computation
  Divergence Operation Lowering
    Normalizes divergence operations by rewriting them into equivalent branch-based control flow
A
B
C
E
E
E
D
D`
D``
C
J2
D
A
A
B
C
J1
B
Reconstruction
Original CFG
Reconstructed CFG
Structurized CFG
Structurization

## Slide 12: Middle-end Compiler
Divergence Intrinsic Insertion
  Split and Join Insertion
    Handles divergent branches using vx_split and vx_join instructions
  Loop Predicate Insertion
    Handling divergent loops with vx_pred
LLVM module
Middle-end Compiler
Divergence Management
Optimization and Transformation
Uniformity Analysis
Divergence Management Function Insertion
General Code Optimizations
Divergence Tracker
LLVM module
Blue boxes indicate components extended or implemented for the Vortex GPU

## Slide 13: Back-end Compiler
Target-specific optimizations and final code generation
  Built on the RISC-V target compiler
  Extends the ISA table with Vortex-specific ISA extensions
  Generates binaries for Vortex GPUs
Vortex Binary
Back-end Compiler
Target Code Generation and Optimization
Vortex ISA Table
LLVM module
Blue boxes indicate components extended or implemented for the Vortex GPU

## Slide 14: VOLT for Vortex 3.0
New version v1.1 is released in Git repo.
Our tool is available in our Git repository
  https://github.com/vortexgpgpu/Volt
CUDA 12.1 and OpenCL 3.0
Provides an end-to-end PoCL / CuPBoP / LLVM compilation pipeline

## Slide 15: CuPBoP Support for Vortex 3.0
Support vortex v3.0 + tools-v3.0.1
  Same CUDA front end. The kernel launch path, toolchain usage and ISA assumptions were updated for Vortex 3.0 SimX and RTL simulation
Expose 3.0 hardware exposed to CUDA programs
  Tensor Core Unit: mma.sync / wmma / ldmatrix → TCU instructions, with a software fallback.
  Types: f16 (f16/f32 accumulate), bf16, tf32, int8, fp8, f64
  wgmma (sm_90a) kernels, with TMA-style tile loads mapped to the DXA engine
  cp.async (synchronous copy), mbarrier and bulk copy under the 1:1 mapping
CI suite
  about 40 CUDA applications (Rodinia-style + TCU/DXA/wgmma samples) × CuPBoP schedules, plus
  warp, named-barrier and async test suites

## Slide 16: Guide for VOLT Extensions
Tutorial 1: Extending kernel functions
Tutorial 2: Extending host functions
Tutorial 3: Extending memory support with the Vortex memory hierarchy
Tutorial 4: Extending CuBBoP support with Tensor Cores, wgmma and DXA on Vortex 3.0
All tutorials include documentation under /Docs
Runnable examples are available under /Tests

## Slide 17: Tutorial 1: Extending Kernel Functions
Expose GPU-specific kernel operations through existing compiler extension points
17
PoCL / OpenCL
pocl_vx_shfl_up(...) → Vortex shfl.up
1 Declare in _clang_opencl.h
2 Implement Vortex built-in library
3 Link into the OpenCL kernel
CuPBoP / CUDA
__reduce_add_sync(...) → warp reduction
1 Match NVVM reduction intrinsic
llvm.nvvm.redux.sync.add
2 Redirect to a runtime helper
3 Use 5× vx_shfl_bfly
./run.sh --baseline [build fails] ./run.sh [both examples PASS]
Source: Volt v1.1 · docs/7.1.tutorial_kernel_extension.md

## Slide 18: Tutorial 2: Extending Host Functions
CUDA application code is unchanged; CuPBoP adapts runtime and launch semantics
18
Existing CUDA host APIs
cudaMemcpy(dst, src, n, kind)
Host staging → vx_copy_to_dev
cudaMemcpyToSymbol(...)
Record bytes → launch args → wrapper
New API: cudaMemGetInfo
cudaMemGetInfo(&free, &total)
vx_mem_info(device, &free, &used)
total = free + used
Only host runtime + header; no kernel translator edit
./run.sh --baseline [link fails] ./run.sh [memory checks PASS]
Source: Volt v1.1 · docs/7.2.tutorial_host_extension.md

## Slide 19: Tutorial 3: Extending Memory Lowering
The same CUDA __shared__ variable can use different Vortex memory resources
19
Select the lowering policy (SCHEDULE=2)
LOCALMEM=0
Global memory
cached by L1 / L2
LOCALMEM=1
Local memory
per-core LMEM
LOCALMEM=2
Size-aware
≤ 16 KB → local
Where to extend
memory_hierarchy.cpp
Add mem_share2auto_sche_2
init.cpp
Select the pass with the LOCALMEM flag
./run.sh [compare LOCALMEM 0 / 1 / 2] BUDGET=32768 ./run.sh nw
Source: Volt v1.1 · docs/7.3.tutorial_shared_memory.md

## Slide 20: Tutorial 4: Tensor Cores, WGMMA and DXA
CuPBoP translates tensor computation and tile movement to Vortex 3.0 hardware
20
WMMA → TCU
CUDA wmma helpers
Runtime wmma_context
TCU matrix multiply
WGMMA → TCU
Hopper wgmma.mma_async
Synchronous lowering
Descriptor + layout conversion
DXA → Tile Copies
Host descriptor programming
2-D global → local
expect_tx + barrier
./run.sh [TCU + DXA SimX GEMM experiments E1 / E2 / E3]
Source: Volt v1.1 · docs/7.4.tutorial_tensor_core.md

## Slide 21: 2026 Publications
Inside VOLT: Designing an Open-Source GPU Compiler
  Shinnung Jeong, Chihyo Ahn, Huanzhi Pu, Jisheng Zhao, Hyesoon Kim, Blaise Tine The ACM SIGPLAN 2026 International Conference on Compiler Construction (CC), Feb 2026
FastTrackGPU: Static-Analysis–Guided Analytical Modeling for Softcore GPUs
  Chihyo Ahn, Shinnung Jeong, Liam Paul Cooper, Ruobing Han, Huanzhi Pu, Nicholas Parnenzini, Jisheng Zhao, Blaise Tine, Hyesoon Kim IEEE Computer Architecture Letters (CAL), 2026
Toward End-to-End ML Support on Vortex
  Shinnung Jeong, Chihyo Ahn, Sai Hemanth Reddy Bheemreddy,Liam Cooper, Krishil Gandhi, Chulhyung Park, Vincent Pham, Huanzhi Pu, Saurabh Singh, Mitul Tandon, Jisheng Zhao, and Hyesoon Kim Open-Source Computer Architecture Research (OSCAR), 2026
CuLifter: Lifting GPU Binaries to Typed IR
  Jisheng Zhao*, Huanzhi Pu*, Shinnung Jeong, Chihyo Ahn, and Hyesoon Kim 59th IEEE/ACM International Symposium on Microarchitecture® (MICRO), 2026

## Slide 22: CuLifter (Micro26, Day 2 Session 6A)
GPU Binary Type Recovery
  Identify type recovery as the central challenge of GPU binary lifting
SIMT-Aware Structure Reconstruction
  Recover control flow and SSA from SASS, handling SIMT-specific constructs and multi-instruction patterns
End-to-End SASS-to-LLVM IR Lifting
  Support multiple GPU generations (SM75–SM120), enabling compiler analysis and cross-platform
Comprehensive Evaluation
  11,977 kernels across 8 benchmark suites, achieving 96.3% exe correctness among 3,584 kernels

## Slide 23: Thank you https://github.com/vortexgpgpu/Volt