## Slide 1: GPGPU Background
Hyesoon Kim

## Slide 2: CPU pipeline
CPU pipeline
Increasing the performance in the execution units
  Increase the issue width (superscalar)
  Multi-threading
Memory
Front-end
Decode
Rename
Schedule
Execution
Write-back
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
5-stage pipeline
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
Superscalar
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
Multi-threading

## Slide 3: GPU pipeline
Warp/Wave-front execution model
SPMD programming model (Single Program Multiple Data)
Inst 1
Inst 2
Inst 3
T1
Inst 1
Inst 2
Inst 3
T2
T3
T4
All threads have the same program
T
T
T
T
One warp
T
T
T
T
Fetch 1 instruction and each instruction has multiple threads are associated.
The group of instruction is called warp/wave-front
Tn
…
T
T
T
T
One warp
T
T
T
T

## Slide 4: GPGPU Programming
Become popular with CUDA (Compute Unified Device Architecture)
CUDA (Based on Nvidia architectures)
  Portland Group Compiler supports CUDA  x86
OpenCL

## Slide 5: Quick Summary of CUDA Programming Model
SIMD or SIMT
  Single instruction multiple data or single instruction multiple thread
Unified Memory space (global memory space)
Program hierarchy
  Thread, block, kernel

## Slide 6: Execution Model
Thread & Block
Inst 1
Inst 2
Inst 3
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
SM
SM
Shared Memory
SP
SP
SP
SP
Shared Memory
SP
SP
SP
SP
Block
Kernel
Block
warp
warp
warp
Sing instruction multiple thread
Block = a group of thread which share “the shared memory space”
Warp
warp
warp
warp
[the slide is from Hong&Kim ISCA’09]

## Slide 7: Memory Data Indexing
SIMT-execution model
Use thread id and block id to index data
Let’s assume N=16, blockDim=4  4 blocks
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
blockIdx.x = 0
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 0,1,2,3
blockIdx.x = 1
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 4,5,6,7
+
blockIdx.x = 2
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 8,9,10,11
blockIdx.x = 3
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 12,13,14,15
+
+
+
+

## Slide 8: 1D, 2D, 3D data structures
A kernel is executed as a grid of thread blocks
Threads and blocks have IDs
  So each thread can decide what data to work on
  Block ID: 1D or 2D
  Thread ID: 1D, 2D, or 3D
Loop index in sequential loop
  Use thread ids, block ids
  1D array index= c1*threadId.x + c2*block Id.x
  2D array index = c1*threadId.x+c2*blockId.x+c3*threadId.y+c4*blockId.y
for (ii = 0; ii < 100; ++ii) {
C[ii] = A[ii] + B[ii];
}
// there are 100 threads
__global__ void KernelFunction(…) {
int tid = blockDim.x * blockIdx.x + threadIdx.x;
int varA = aa[tid];
int varB = bb[tid];
C[tid] = varA + varB;
}
CPU code
CUDA code

## Slide 9: Memory Space
 | Space | ~= CPU
Local Memory | Within Threads | Stack
Shared Memory | Within Blocks | Distributed memory space
Global Memory | All | Centralized storage
Constant Memory | All | Centralized read-only storage (very small)
Texture Memory | All | Centralized read-only storage (medium size, 2D- cache)
Thread, block, and kernel have different memory spaces

## Slide 10: CUDA Program Example

## Slide 11: Number of Threads Per CUDA Block
Host sets the number of threads per CUDA block. E.g., threadsPerBlock
Set up at the kernel launch time
# of registers per CUDA block
  Compiler sets how many architecture registers are needed for each CUDA block (Will be covered later part of the course)
  Typical CPU ISAs, # of registers per thread is fixed (e.g., 32), but in CUDA, this is flexible
Shared memory size is determined from the code
E.g., __shared__ int sharedMemory[1000];  4B*1000 = 4000B
kernelName<<<numBlocks, threadsPerBlock>>>(arguments);

## Slide 12: Shared Memory
From: http://accel.cs.vt.edu/files/lecture10.pdf

## Slide 13: Synchronization Model
Bulk-Synchronous Parallel (BSP) program (Valiant [90])
Synchronization within blocks using explicit barrier
Implicit barrier across kernels
  Kernel 1  Kernel 2
  C.f.) Cuda 3.x
barrier
Block
barrier
Block
barrier
barrier
Block
barrier
Block
barrier
Block
Kernel1
Kernel2
Barrier

## Slide 14: OpenCL vs. CUDA
 | OpenCL | CUDA
Execution Model | Work-groups/work-items | Block/Thread
Memory model | Global/constant/local/private | Global/constant/shared/local + Texture
Memory consistency | Weak consistency | Weak consistency
Synchronization | Synchronization using a work-group barrier (between work-items) | Using synch_threads Between threads

## Slide 15: GPU Pipeline
Fetch
  One instruction for each warp
  Multiple PC registers exist to support multi-threaded architecture
  Round-robin scheduler
Wide execution width
Scheduler
I-cache
Fetch unit
Decoder
. . . . . .
Memory access unit
. . . . . .
Writeback
Memory
Lane 0
Lane 1
Lane N-1
Lane 0
Lane 1
Lane N-1
Active bit mask vectors/
score boarding
Register
Scheduler (Score boarding)

## Slide 16: GPU Register Files
To accommodate a large number of active threads, a large number of register files are essential.
e.g.) 128 threads, 64 registers = 128X64 = 8KB
NVIDIA G80 architecture: 64KB registers (16KB cache)
Vortex: 32x # of threads per warp x # of warps x # or cores
Register read BW
1Tflop/s peak performance (2 read, 1 write)
  -2T * 32B/s = 64TB/s register read BW
Highly banked register files

## Slide 17: Register File Structures: Multiple Banks
. . . . . .
. . . . . .
. . . . . .
Register files
. . . . . .
Lane 0
Lane 1
Lane N-1
Warp 0’s reg file
Warp M-1’s reg file
Warp ID.Reg ID
. . .
Th 0
…
Th N-1
Writeback
Multiple banks (Narasiman’s figure)
All threads in a warp read the register values in parallel.
Register is indexed with register ID, warp ID

## Slide 18: Handling Branch Instructions
A reduction example
What about other threads?
What about different paths?
0
1
2
3
4
5
6
7
0
2
4
6
0
4
0
If (threadId.x%==2)
If (threadId.x%==4)
If (threadId.x%==8)
A
B
C
D
If (threadid.x>2) {
do work B}
else {
do work C
}
From Fung et al. MICRO ‘07
Divergent branch!

## Slide 19: Split/Join
Compiler inserts split/join
Split:
  Put tmask in the ipdom stack (do work c part}
  Put next PC in the stack (not-taken path. // do work c part )
Join
  Pop from a stack
If (threadid.x>2)
// split
{
do work B
}
else {
// join
do work C
}

## Slide 20: How Many CUDA Blocks on One Stream Multiprocessor?
SM
SM
SM
Cache
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
  How many CUDA blocks can run on one streaming multiprocessor?
  Multiple blocks per SM
Grid 0
Block (2,0)
Block (0,1)
Block (1,1)
Block (2,1)
2 to 1?
3 to 1?
Block (0,0)
Block (1,0)
Occupancy

## Slide 21: Occupancy
How many CUDA blocks can be executed on one SM is decided by following parameters
  # of registers, shared memory, # of threads
Exact H/W configurations are varied by GPU microarchitecture
E.g., HW: each SM can execute 256 threads, 64K registers, 32 KB shared memory
  SW: one CUDA block: 32 threads and 2KB shared memory and each thread has 64 registers
  Constrain by running threads: 256/32 = 8 CUDA blocks
  Constrain by register size = 64*1024/(64*32) = 32 CUDA blocks
  Constrain by shared memory = 32KB/2KB = 16 CUDA blocks
  Final answer: 8 CUDA blocks per SM

## Slide 22: Why Do We Care about Occupancy?
Higher Occupancy means more parallelism.
Utilization: Utilizing more hardware resources generally leads to better performance.
Exceptional cases will be studied in later lectures.
SM
SM
SM
SM
Block
Block
Block
Block
SM
Block
Block
SM
Block
Block
SM
Block
Block
Case (a): Each SM runs one CUDA block (6 threads per block)
Case (b): Each SM runs two CUDA block (4 threads per block)
SM
Block
Block

## Slide 23: GPU Pipeline (1)
 | PC value
#1 (b:1, T1-T4) | 0x8000
#2 (b:1, T5-T8) | 0x8004
#3 (b:2, T1-T4) | 0x8000
#4 (b:2, T5-T8) | 0x800A
I-cache
Front-end
Decode
Memory
RF
Execution
Write-back
schedule
Shared Memory
0x8000 | add r1, r1, 1
0x8004 | sub r2, r,2,1
0x8008 | mov r1, tid.x
0x800A | mov r2, ctaid.x
0x8010 | ld.shared r1 [A]
tid.x: special register to store thread ID within a block
ctaid.x: special register to store block ID within a grid
 | Th1 | Th2 | Th3 | Th4
R1 | 11 | 12 | 13 | 14
R2 | 2 | 2 | 2 | 2
R3 | 3 | 4 | 13 | 15
R4 | 23 | 24 | 32 | 33
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
1
1
1
1
11
12
13
14
12
13
14
15
add r1, r1, 1
add r1, r1, 1
add r1, r1, 1
add r1, r1, 1
add r1, r1, 1
add r1, r1, 1

## Slide 24: GPU Pipeline (2)
 | PC value
#1 (b:1, T1-T4) | 0x8000
#2 (b:1, T5-T8) | 0x8004
#3 (b:2, T1-T4) | 0x8000
#4 (b:2, T5-T8) | 0x800A
I-cache
Front-end
Decode
Memory
RF
Execution
Write-back
schedule
Shared Memory
0x8000 | add r1, r1, 1
0x8004 | sub r2, r,2,1
0x8008 | mov r1, tid.x
0x800A | mov r2, ctaid.x
0x8010 | ld.shared r1 [A]
tid.x: special register to store thread ID within a block
ctaid.x: special register to store block ID within a grid
 | Th1 | Th2 | Th3 | Th4 | Th5 | Th6 | Th7 | Th8
R1 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
R2 | 3 | 3 | 3 | 3 | 2 | 2 | 2 | 2
R3 | 3 | 4 | 13 | 15 | 23 | 32 | 37 | 23
R4 | 23 | 24 | 32 | 33 | 11 | 7 | 8 | 5
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
1
1
1
1
2
2
2
sub r2, r2, 1
1
1
1
sub r2, r2, 1
sub r2, r2, 1
sub r2, r2, 1
sub r2, r2, 1
One lane is not shown

## Slide 25: GPU Pipeline (3)
 | PC value
#1 (b:1, T1-T4) | 0x8000
#2 (b:1, T5-T8) | 0x8004
#3 (b:2, T1-T4) | 0x8000
#4 (b:2, T5-T8) | 0x800A
I-cache
Front-end
Decode
Memory
RF
Execution
Write-back
schedule
Shared Memory
0x8000 | add r1, r1, 1
0x8004 | sub r2, r,2,1
0x8008 | mov r1, tid.x
0x800A | mov r2, ctaid.x
0x8010 | ld.shared r1 [A]
tid.x: special register to store thread ID within a block
ctaid.x: special register to store block ID within a grid
 | Th1 | Th2 | Th3 | Th4 | Th5 | Th6 | Th7 | Th8
R1 |  |  |  |  |  |  |  | 
R2 |  |  |  |  |  |  |  | 
R3 |  |  |  |  |  |  |  | 
R4 |  |  |  |  |  |  |  | 
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
2
2
2
2
2
2
2
mov r2, ctaid.x
One lane is not shown
Block 2 register file

## Slide 26: GPU Pipeline (4)
 | PC value
#1 (b:1, T1-T4) | 0x8000
#2 (b:1, T5-T8) | 0x8004
#3 (b:2, T1-T4) | 0x8000
#4 (b:2, T5-T8) | 0x8008
I-cache
Front-end
Decode
Memory
RF
Execution
Write-back
schedule
Shared Memory
0x8000 | add r1, r1, 1
0x8004 | sub r2, r,2,1
0x8008 | mov r1, tid.x
0x800A | mov r2, ctaid.x
0x8010 | ld.shared r1 [A]
tid.x: special register to store thread ID within a block
ctaid.x: special register to store block ID within a grid
 | Th1 | Th2 | Th3 | Th4 | Th5 | Th6 | Th7 | Th8
R1 |  |  |  |  |  |  |  | 
R2 |  |  |  |  |  |  |  | 
R3 |  |  |  |  |  |  |  | 
R4 |  |  |  |  |  |  |  | 
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
5
6
7
8
6
7
8
mov r2, ctaid.x
One lane is not shown
Block 2 register file

## Slide 27: Mask Bits
What if we do not need to execute all 4 threads?
Mask bits tell which threads are active.
 | Src 1 |  | Src 2 | 
w1 | v | r | v | r
w2 | v | r | v | r
w3 | v | r | v | r
w4 | v | r | v | r
w5 | v | r | v | r
 | Src 1 |  | Src 2 | 
w1 | v | r | v | r
w2 | v | r | v | r
w3 | v | r | v | r
w4 | v | r | v | r
w5 | v | r | v | r
 | Src 1 |  | Src 2 | 
w1 | v | r | v | r
w2 | v | r | v | r
w3 | v | r | v | r
w4 | v | r | v | r
w5 | v | r | v | r
 | Src 1 |  | Src 2 | 
w1 | v | r | v | r
w2 | v | r | v | r
w3 | v | r | v | r
w4 | v | r | v | r
w5 | v | r | v | r
V
V
V
V
V
V
V
V
id | Mask bit
w1 | 1111
w2 | 1110
w3 | 0111
w4 | 1111
w5 | 1111
V
V
V
V
V
V
V
V
V
V

## Slide 28: Summary
GPUs execute many threads as a group (warp/wave front)
GPU provides features to handle multiple threads concurrently and also time multiplexing
Massive thread level parallelism  massive memory level parallelism