## Slide 1: Vortex Micro Architecture
Presenter: Blaise Tine
Notes: Narration:
This poster presents Vortex, a reconfigurable and scalable RISC-V GPGPU accelerator.
Vortex’s main goal is to use RISC-V to utilize the advantages of SIMT execution model and provide a customizable design to facilitate architecture research.
In addition, we show that a minimal set of 5 instructions is enough to achieve a highly parallel execution model on RISC-V.
Single Instruction Multiple Threads execution model, or SIMT, has the advantage of having a scalar based programming model, which makes it easier to program on.
Through POCL, an open-source framework to implement the compiler and runtime software for OpenCL, we were able to execute unmodified OpenCL kernels on Vortex.
We achieved that by linking POCL with Vortex's runtime kernel, which provides warp and thread creation, warp barriers, and control divergence.
Vortex microarchitecture has two main configuration methods to scale for various application domains: increasing the number of parallel work-items and configuring the cache system. Each one of these methods has its own unique trade-offs, both in terms of performance for different applications and hardware and energy cost. The first method is to increase the parallel work-items in the design by either increasing the number of threads per warp, number of warps per core, number of cores per clusters, and the number of clusters. The second method is by configuring the cache system. Our L1, shared memory, L2, and L3 are all based on the same high-throughput banked design that supports a snoop protocol and prefetching.
We have evaluated our design both 15 nm educational library and Arria 10 Intel FPGA on a subset of Rhodina benchmarks and were able to achieve frequencies of 300 MHz and 192 MHz respectively.
In addition, we were able to fit a 2 cluster 8 core configuration with a total of 256 work units on Arria 10 Intel FPGA.
We also used the OPAE open-source accelerator API to be able to execute OpenCL kernels on the FPGA.

## Slide 2: Agenda
  ISA Extension
  GPGPU Microarchitecture
  High-Bandwidth Caches
  Texture Units

## Slide 3: Vortex GPGPU Platform
Hardware
  Fully configurable multi-core GPU
  PCIe host-device interface
  Up to 32-cores @ 200 MHz
  Caches & shared Memory
  Floating-point Units
  Hardware texture units
Open-source toolchain
  POCL: OpenCL
  SwiftShader : OpenGL
  OPAE: FPGA Driver API
  Verilator: RTL simulation
  Yosys: FPGA Synthesis

## Slide 4: RISC-V ISA Extension for Vortex
Threading model
  Wavefronts
  Threads
Memory model
  Global memory
  Shared memory
Register File
  Use RISC-V Int/float registers
  No predication
Synchronization
  Use RISC-V fence

## Slide 5: Vortex GPU Microarchitecture
Five-stage RISC-V Pipeline
  IF | ID | Issue | EX | Commit
  In-order issue / out-of-order commit
  Single-precision FPU

## Slide 6: Vortex GPU Microarchitecture (2)
Five-stage RISC-V Pipeline
  IF | ID | Issue | EX | Commit
  In-order issue / out-of-order commit
  Single-precision FPU
  Wavefront Scheduler
  Instruction Buffer
  GPGPU Execute Unit
  Shared Memory
  Texture Units

## Slide 7: Vortex GPU Microarchitecture (3)
Clustering
  Processor
    [cluster*] [L3 cache]
      [core*] [L2 cache]

## Slide 8: Vortex GPU Microarchitecture (4)
AFU Command Processor
  Local DRAM access
  Host CPU-GPU communication
    Data transfer
    GPU control & status

## Slide 9: Vortex GPU Microarchitecture (5)
Fetch
  Issue ICache request
  (PC, wid, tmask)
Decode
  Decode instruction into Ibuffer
  (instr, wid, tmask)
Issue
  Issue instruction to execute unit
  (instr, regs, wid, tmask)
Writeback
  Write result into GPRs
  (result, wid, tmask)
PC wid tmask
instr
wid
tmask
instr
regs wid tmask
result
wid
tmask

## Slide 10: Vortex High-bandwidth Caches
Design goals
  High-bandwidth transactions
  Non-blocking operation
  Highly Configurable
Challenges
  Handling bank conflicts
  FPGA constraints
    SRAM ports
    Area cost

## Slide 11: Vortex High-bandwidth Caches (2)
Reducing bank conflicts on GPU
  Coalescing aligned memory addresses
  Takes place inside the LSU
Design shortcomings for Vortex
  LSU and Cache Intra-dependency
  LSU overhead
  Cache request overhead
  Shared memory doesn’t need coalescing
    Unnecessary delay cycle
  L2/L3 caches also have bank conflicts
11

## Slide 12: Vortex High-bandwidth Caches (3)
Our solution: Virtual multi-porting
  Perform coalescing inside the cache
How?
  Add virtual ports to each bank
  Ports hold requests to same line
Advantages
  No cycle overhead
    Added to the bank select logic
  Maximize cache line read access
  Minimal storage overhead in MSHR
  Reuse exiting SRAM port
  Configurable number ports
    Area vs Perf.
Tag Access
Tag Access
CL1
CL2
CL3
CL3
Bank
Conflict!
AddrA
AddrB
AddrC
AddrD
Tag Access
Tag Access
Bank select
And
Coalescing
ARB
ARB
ARB
ARB
Pipeline Register
Pipeline Register
Data Access
Data Access
Data Access
Data Access
Pipeline Register
Core
Response
Merge

## Slide 13: Vortex Texture Units
Motivation
  Accelerating texture filtering
Application
  Image processing: OpenVX, OpenCL
  2D,3D graphics: OpenVG, OpenGL
Texture filtering complexity
  Memory bound
    Quad texels fetch
    Mipmapping
  Compute bound
    Texture sampling
      linear, bilinear, trilinear
13
13
13
Vortex Rendering
Texture Sampling
Kernel

## Slide 14: Vortex Texture Units (2)
Texture unit configuration
  Use RISC-V unused CSRs
  Store per-miplevel texture info
    Dimensions and format
    Addressing mode
    Filtering mode

## Slide 15: Vortex Texture Units (3)
Address Generation
  Calculate texture addresses
  Apply Addressing mode
Memory Scheduler
  Detect duplicate addresses
  Schedule memory requests
  Gather texel results
Texel Sampler
  Decode texture format
  Apply texture sampling

## Slide 16
Thank You!