## Slide 1: Vortex-Drone Introduction and Tutorial
Sam Jijina
HPArch Research Lab
Georgia Institute of Technology
OAC 2103951

## Slide 2: Motivation
Commercial drone industry will reach 805,000 in sales in 2021-2022, a CAGR of 51% [1]
Increasing use cases of drones from surveying land to emergency services and national security
Open-source flight stack to promote innovation through collaboration
Characterizing underlying architecture and flight stack to achieve high reliability, safety, and performance
Intelligence, Business Insider. “Commercial Unmanned Aerial Vehicle (UAV) Market Analysis – Industry Trends, Forecasts and Companies.” Business Insider, Business Insider, 10 Feb. 2020, www.businessinsider.com/commercial-uav-market-analysis.
Notes: https://www.businessinsider.com/commercial-uav-market-analysis
https://www.faa.gov/data_research/aviation/aerospace_forecasts/media/Unmanned_Aircraft_Systems.pdf

## Slide 3: Applications of Drone Technology
Aerial photography
Agriculture
Defense
Emergency services
Geographic mapping
Personal hobby
Search and rescue
Shipping
and many more...
Notes: https://medium.com/remote-sensing-in-agriculture/how-drone-technology-can-be-leveraged-in-agriculture-54b687c6dc45
https://www.steamboatpilot.com/news/the-sky-is-the-limit-routt-county-invests-in-drone-technology-for-law-enforcement-and-wildfires-as-legal-groups-worry-about-becoming-a-surveillance-society/
http://blog.jammer-store.com/2012/05/police-of-victoria-australia-will-use-flying-spy-drones/

## Slide 4: Current Drone Technologies
DJI Commercial Drones [5]
  Matrice Series (customizable and weight carrying configuration)
DJI Personal Drones [7]
  Spark
  Mavic Series
Parrot Personal Drones [8]
Amazon Delivery Drones [6]
SkyDio Series [9]
  These drones are specialised for tracking moving objects
  They heavily rely on Computer Vision and Localisation utilities
Boeing and Lockheed Martin [10], [11]
  Drones are oriented more towards defense sector
  High Altitude Long Endurance (HALE)
  Stalker XE UAS
Notes: ***add images of current drone tech in the world, background information/ current tech details and their applications
https://www.dji.com/matrice-200-series
https://www.support.com/how-to/how-to-use-the-camera-for-a-dji-spark-drone-11760
Citations for Text (DJI, AMAZON, SKYDIO)

## Slide 5: Current Technological Shortcomings
Most drone flight stacks are not open-source
No access to the autopilot code base
Weight carrying capacity limitations
Very difficult to alter hardware due to custom PCBs
Not cost effective for various types of research projects

## Slide 6: Design Choices
Open-source drones already exist
  CrazyFlie [12]
  PlutoX [13]
BUT…
  Limited weight carrying capacity
  Limited flight time due to battery capacity
  Microcontroller performance limitation
We set up a development platform to allow for more sensors and devices to be added in the future
  Camera for SLAM [14] or OpenCV [15]
  LIDAR
So we decided to use a frame kit
to build a custom drone

## Slide 7: Build Process
Steps:
Component collection and compatibility validation
  Motor specification calculations
    Dependent on aggregate weight
    Weight carrying capacity
    Motor power calculations
Choose flight controller
  Pixhawk 4 [17], Navio2 [16], Pixhawk Pro [17]
  Based on drone purpose
  Cost analysis
  Performance criteria
  We needed a low latency flight controller which would work with an on-board computer (Raspberry Pi) [18]
Notes: https://www.amazon.com/gp/product/B00N3I9GM4/ref=ppx_yo_dt_b_asin_title_o05_s01?ie=UTF8&psc=1
https://docs.px4.io/v1.9.0/en/flight_controller/pixhawk3_pro.html

## Slide 8: Architecture of Drone Flight Stack
Path Planning and SLAM
Notes: https://www.amazon.com/gp/product/B00N3I9GM4/ref=ppx_yo_dt_b_asin_title_o05_s01?ie=UTF8&psc=1

## Slide 9: Hardware Overview
Raspberry Pi 3 Model B +
Emlid Navio2 HAT for Pi
ESCs (Electronic Speed Control)
935KV motors
GPS/GLONASS receiver
3000 mAh 3S LiPo battery
915 MHz Ground-to-Air Telemetry communication
Features of Navio2:
  Dual IMU
  Triple redundant power supply
  High resolution barometer

## Slide 10: Navio2 HAT Setup
ESCs
Motors
915 MHz Telemetry
Battery
PPM
Encoder
GPS Antenna
Notes: how we built the drone will be discussed here, Why did you made choices for your current drone (HW, SW, Battery)
https://www.amazon.com/gp/product/B00N3I9GM4/ref=ppx_yo_dt_b_asin_title_o05_s01?ie=UTF8&psc=1
https://docs.px4.io/v1.9.0/en/flight_controller/pixhawk3_pro.html

## Slide 11: Flight Controller - GCS
Two types of software:
  Ground Control Station
  Autopilot firmware
Ground Control Station (GCS)
  Executes from laptop
  Real-time data (altitude, speed, location, battery)
  Telemetry communication
  Remote commands to override erroneous behavior
Most popular GCS is MissionPlanner [20]
  Open-source
  Actively maintained

## Slide 12: Flight Controller - Autopilot
ArduCopter (fork of ArduPilot) [21]
  Executes on board the drone
  Interfacing between hardware and flight code
  Autonomous flight capabilities
  Flight modes (Guided, Auto, Acro)
  Sensor polling and attribute actuation

## Slide 13: Flight Controller – Comms
MAVLink [22]
  Micro Air Vehicle Link
  Data packet protocol which enables standardized communication between multiple drones
  Issuing commands to a drone
DroneKit API [23]
  Python and C++ APIs to issue flight commands easily
  Converts commands to MAVLink protocol
  Enables use of Python AI libraries with drone

## Slide 14: Drone Operating System
Real Time Operating System (RTOS)
  RTOSs are used in time critical applications
  Popular in robotics
  Minimal, if any, latency in response
  Kernel tasks can be pre-empted
Most fully supported RTOSs are not open-source
We had the choice of using Linux [25] or Robot Operating System (ROS) [24]
  ROS is a specialized OS for robotics
  Due to the availability of community support and documentation, we decided to use Linux
  PREEMPT_RT patch

## Slide 15: General UAV Task Outline
Capture images
  Various image sensors
  Buffer video feed
Run computations on images
  3D Reconstruction
  Feature detection
  Collision avoidance
Communicate data and results
  Distributed workload
  Different communication technologies
  Communicate tasks time vary significantly
Dependencies exist between the tasks
DroneEye
(Photo: DSC IITP)
Notes: A drone’s workload in the aforementioned applications, usually is split between capture, compute, and communicate subtasks.
There can be many dependencies between those tasks. But for a given workload, neither the capture task nor the compute task is flexible in terms of time needed to completion. However, the communicate task’s time can vary quite significantly and hence careful choice of communication technology is important. The upcoming millimeter wave technology offers great promise in this regard.

## Slide 16: Flight Testing Methods
Manual Flying and Testing
  Weather dependent
  Battery limitation
  Approval Process
Simulations
  Software in the Loop (SITL)
  Hardware in the Loop (HITL)
SITL simulations used to test flight code
  ArduCopter natively compiles for SITL simulation
  Less system resource heavy
Microsoft AirSim [27] for HITL simulation
  Open-source
  System resource heavy
  Provides environment simulation (neighborhood, city)
Notes: https://tipsfordrones.com/can-drones-fly-in-rain/

## Slide 17: ArduPilot codebase
Vehicle code
  Copter, Plane
  Sub, etc.
Shared libraries
  Sensors
  GPS, PID, EKF
Hardware Abstraction Layer
Tools
  Sims
  Auto-test
  Logging
Code Structure (Photo: ArduPilot org)

## Slide 18: ArduCopter
Interface between higher level code and H/W
Handles inner-loop control (flight attitude, motor imperfection, GPS sync)
Main flight “brains” of the drone
  Flight algorithms
  Sensor fusion

## Slide 19: SITL Simulation Steps
System Requirements
  x86 ISA
  Discreet GPU
  Ubuntu 18+
  8GB RAM
Get the ArduPilot codebase & build
  git clone https://github.com/ArduPilot/ardupilot
  Tools/environment_install/install-prereqs-ubuntu.sh –y
  cd ardupilot/ArduCopter
  sim_vehicle.py –w
  sim_vehicle.py --console –map
DroneKit python API for drone commands
  https://github.com/dronekit/dronekit-python

## Slide 20: SITL Simulation Demo

## Slide 21: Vortex + Drone (1)
Heterogenous UAV Stack

## Slide 22: Vortex + Drone (2)
Vortex accelerator for UAV stack
  Rapid processing of video frames
  Custom ML modelling
Flight controller (FC) frequency approx. 200MHz
  Front end accelerated, flight controller bottleneck?
  Exploring processor reliability for RISC-V based FC
Standard MAVLink comm. protocol
ESC profiling and design
HITL Simulation using Microsoft AirSim

## Slide 23: Thank You

## Slide 25: References
https://www.businessinsider.com/commercial-uav-market-analysis
https://medium.com/remote-sensing-in-agriculture/how-drone-technology-can-be-leveraged-in-agriculture-54b687c6dc45 (Slide 2)
https://www.steamboatpilot.com/news/the-sky-is-the-limit-routt-county-invests-in-drone-technology-for-law-enforcement-and-wildfires-as-legal-groups-worry-about-becoming-a-surveillance-society/ (Slide 2)
http://blog.jammer-store.com/2012/05/police-of-victoria-australia-will-use-flying-spy-drones/ (Slide 2)
https://www.dji.com/matrice-200-series
https://www.amazon.com/Amazon-Prime-Air/b?ie=UTF8&node=8037720011
https://store.dji.com/?gclid=Cj0KCQiA4sjyBRC5ARIsAEHsELFkQcKySwGljteaiXuFpDptFahOJOMxK9aHhbYcHsh5E-mlrKLn-zIaAmqSEALw_wcB
parrot.com
skydio.com
boeing.com/defense
https://www.lockheedmartin.com/en-us/capabilities/autonomous-unmanned-systems.html
bitcraze.io
https://www.dronaaviation.com/plutox/
https://arxiv.org/abs/1502.00956
opencv.org
emlid.com/navio2
pixhawk.org
raspberrypi.org
https://docs.emlid.com/navio2/ardupilot/typical-setup-schemes/(Slide 10)
ardupilot.org/planner
ardupilot.org/copter
mavlink.io
dronekit.io
ros.org
linux.org
https://dl.djicdn.com/downloads/inspire_1/en/Firmware_Update_Guide_en_v1.4.pdf
https://github.com/microsoft/AirSim
https://www.support.com/how-to/how-to-use-the-camera-for-a-dji-spark-drone-11760
https://www.amazon.com/gp/product/B00N3I9GM4/ref=ppx_yo_dt_b_asin_title_o05_s01?ie=UTF8&psc=1
https://docs.px4.io/v1.9.0/en/flight_controller/pixhawk3_pro.html
https://tipsfordrones.com/can-drones-fly-in-rain/
Notes: **Fix this