## Slide 1: Vortex Microarchitecture
Blaise Tine
Notes: Narration:
This poster presents Vortex, a reconfigurable and scalable RISC-V GPGPU accelerator.
Vortex’s main goal is to use RISC-V to utilize the advantages of SIMT execution model and provide a customizable design to facilitate architecture research.
In addition, we show that a minimal set of 5 instructions is enough to achieve a highly parallel execution model on RISC-V.
Single Instruction Multiple Threads execution model, or SIMT, has the advantage of having a scalar based programming model, which makes it easier to program on.
Through POCL, an open-source framework to implement the compiler and runtime software for OpenCL, we were able to execute unmodified OpenCL kernels on Vortex.
We achieved that by linking POCL with Vortex's runtime kernel, which provides warp and thread creation, warp barriers, and control divergence.
Vortex microarchitecture has two main configuration methods to scale for various application domains: increasing the number of parallel work-items and configuring the cache system. Each one of these methods has its own unique trade-offs, both in terms of performance for different applications and hardware and energy cost. The first method is to increase the parallel work-items in the design by either increasing the number of threads per warp, number of warps per core, number of cores per clusters, and the number of clusters. The second method is by configuring the cache system. Our L1, shared memory, L2, and L3 are all based on the same high-throughput banked design that supports a snoop protocol and prefetching.
We have evaluated our design both 15 nm educational library and Arria 10 Intel FPGA on a subset of Rhodina benchmarks and were able to achieve frequencies of 300 MHz and 192 MHz respectively.
In addition, we were able to fit a 2 cluster 8 core configuration with a total of 256 work units on Arria 10 Intel FPGA.
We also used the OPAE open-source accelerator API to be able to execute OpenCL kernels on the FPGA.

## Slide 2: Agenda
  ISA Extension
  Microarchitecture
  Hardware Scaling and Configuration
  High-Bandwidth Caches

## Slide 3: Vortex GPGPU Platform
Hardware
  Fully configurable multi-core GPU
  PCIe host-device interface
  Caches & shared Memory
  Floating-point Units
  32 and 64-bit ISA
Open-source toolchain
  LLVM: Compiler
  POCL: OpenCL
  CuPBoP: CUDA
  OPAE: Intel FPGA API
  XRT: Xilinx FPGA API
  Verilator: RTL simulation
  Yosys: FPGA Synthesis
FPGA Synthesis
  Altera: Arria10, Stratix 10
  Xilinx: Alveo U50, U250, U280, U55

## Slide 4: RISC-V ISA Extension for Vortex
Threading model
  Wavefronts
  Threads
Thread Divergence Handling
  Split/Join stack based
  Thread predication
Memory model
  Global memory
  Shared memory
Register File
  RISC-V Integers and floats
  32 * #warps * #threads regs
Synchronization
  Global and local barriers
  RISC-V fence
Instruction | Description
wspawn #warps, %PC | Wavefronts activation
tmc #threads | Thread mask control
#addr ← split #pred | Control flow divergence
join #addr | Control flow reconvergence
pred #pred, #mask | Thread predication
bar #id, #warps bar #id, #cores | Wavefront local barrier (positive id) Wavefront global barrier (negative id)

## Slide 5: Vortex GPU Microarchitecture
Six-stage RISC-V
in-order issue
out-of-order commit Pipeline

## Slide 6: Vortex GPU Microarchitecture (2)
Schedule Stage
  Warp scheduler
  Warp Table
  IPDOM Table
  Inflight Tracker

## Slide 7: Vortex GPU Microarchitecture (3)
Fetch Stage
  Icache Request
  Deadlock avoidance
    Cacheless only

## Slide 8: Vortex GPU Microarchitecture (4)
Decode Stage
  Decode instruction
  Unlock warp
    !branch
    !csrs
    !wctl

## Slide 9: Vortex GPU Microarchitecture (5)
Issue Stage
  Instruction Buffer
  Scoreboard
  Operands Collector
  Dispatch

## Slide 10: Vortex GPU Microarchitecture (6)
Execute Stage
  ALU cluster
  FPU cluster
  LSU cluster
  SFU cluster

## Slide 11: Vortex GPU Microarchitecture (7)
Commit Stage
  Per-unit gather
  Writeback
  Commit tracker

## Slide 12: GPU Hierarchical Clustering
Socket
  Multiple cores
  Optional L1 cache
Cluster
  Multiple sockets
  Optional L2 cache
Processor
  Global barrier
  Optional L3 cache
FPGA
  Vortex Processor
  Device Controller
  DMA/PCIe Controllers
  Device Memory

## Slide 13: Execute Stage
Dispatch Queues
  Flow control
  Per execute unit
Dispatch Unit
  Read IW x #T data from queue
  Send #Block x #lanes data to array
  Per execute unit
Gather Unit
  Merge outputs from array
  Return IW x #T results
  Per execute unit

## Slide 14: Compute Scaling
Pipeline Configuration
  Number of wavefronts (#W)
  Number of threads (#T)
  Issue width (IW)
Execute Unit Configuration
  Number of blocks (#B)
  Number of lanes (#L)
Dispatch Capacity
  IW * #T total work items
Compute Capacity
  #B * #L total processing element
Full Compute Capacity
  #B=#IW and #L=#T

## Slide 15: Memory Scaling
Load/Store Unit Configuration
  Number of slices (#B)
  Number of lanes (#L)
Dispatch Capacity
  IW * #T total work items
Memory Capacity
  #B * #L total requests
Full Memory Capacity
  #B=#IW and #L=#T

## Slide 16: Vortex High-bandwidth Caches
High-Performance
  Multi-banked
  Non-blocking operation
  Highly Configurable
Highly Configurable
  Banking
  Associativity
  Writeback / Writethrought
  DirtyBytes
  Eviction Policy
  Hierarchical Flush
  Pipeline Queues

## Slide 17
Thank You!