## Slide 1
Using Vortex on FPGA
https://github.com/vortexgpgpu/vortex_tutorials
Presenter: Liam Cooper
Notes: 1

## Slide 2
Overview
Supported platforms
    Intel Quartus, OPAE
    Xilinx XRT
    Yosys
Supported FPGAs
    Altera Arria 10, Stratix 10
    Xilinx Alveo U50, U280
    Xilinx Versal VCK5000
Vortex is synthesizable up to 8 cores, each with 32 warps and 32 threads per warp on Stratix 10
Notes: 2

## Slide 3
Synthesis for Xilinx FPGAs
Requires Xilinx XRT to be installed
The directory hw/syn/xilinx/xrt contains makefile for synthesis
    Vortex hardware configuration and target Xilinx platform passed to makefile
Xilinx hardware emulation supported
vitis_analyzer used for viewing area and timing reports
To run a program on Vortex via FPGA, use blackbox script
    Specify xrt for driver option
Notes: 3

## Slide 4
Synthesis for Altera FPGAs
Requires Intel Quartus and OPAE to be installed
The directory hw/syn/altera/opae contains makefile for synthesis
    Vortex hardware configuration and FPGA family name passed to makefile
Scripts for generating area, power, and timing reports
To run a program on Vortex via FPGA, use blackbox script
    Specify opae for driver option
Notes: 4

## Slide 5
Notes: 5

## Slide 6
Vortex Tutorial Assignments
https://github.com/vortexgpgpu/vortex_tutorials
Presenter: Liam Cooper
Notes: 6

## Slide 7
Pre-exercise Setup: VM Download (Recommended)
Install VirtualBox and Vagrant
Download the Vagrant Box image from the tutorial repo
Add and initialize the Box image
Download the Vagrantfile from the tutorial repo
Boot the VM with vagrant up
Finally, run vagrant ssh to connect to VM
Detailed setup instructions in VM_README.md
Test Vortex:
  ./ci/blackbox.sh --cores=2 --app=demo
Notes: 7

## Slide 8
Pre-exercise Setup: Remote Account in Browser
Log into rg-login.crnch.gatech.edu with provided login
ssh into flubber1
Clone the Vortex repo
Set up the environment variables
Run make
Detailed setup instructions in REMOTE_ACCESS.md
Will be available until the end of the conference
Test Vortex:
    ./ci/blackbox.sh --cores=2 --app=demo
Notes: 8

## Slide 9
6 Tutorial Assignments
Vortex tutorial assignments
  Designed to cover different components of Vortex
  Introduction assignments for RTL: Assignments #1 & #2
  How to modify LSU (lost-store unit) and debug: Assignments #3 & #4
  How to add a custom new instruction: Assignment #5
  Assignments #1 and #2 only explain the steps
  Assignments #3 and #5 provide a solution
    Please use the old VM (the latest repo already includes the solution)
  Assignment #6 is an extension of #1 and #5
Notes: 9

## Slide 10
Blackbox
Vortex's main test driver
Arguments
  Clusters, cores, warps, threads
  L2cache, L3cache
  Driver
    rtlsim, simx, xrt, opae
  Debug
  Perf
  App
    Application to run
  Args
    Arguments to the app
Notes: 10

## Slide 11
Assignment 1
Add a new performance counter for the average number of active threads per cycle
  Check if instruction is being issued
  Count number of active threads in the active thread mask
  Divide total number of active threads by cycle count in driver
Test with output of demo program kernel
Notes: 11

## Slide 12
Assignment 2
Count the number of coalesced memory requests
  GPUs generate multiple memory requests from the same warp/wave front, often with duplicate memory addresses across multiple threads in the warp
  Increment counter in LSU when memory requests in other threads are the same
  Increment only once per warp
Test with output of demo program kernel
Notes: 12

## Slide 13
Assignment 3/4
Add a simple next line prefetcher in LSU
  Every time a load request is computed, generate the next cache line address and send to d-cache
  Request metadata must be stored somewhere so the processor knows the correct memory requested
Assignment 4 verifies implementation by showing how to debug to see if prefetch requests are generated and used correctly
Assignment 3 is already implemented in latest version of Vortex; use VM instead
Notes: 13

## Slide 14
Assignment 5
Add a new instruction for prefetching
  Add an intrinsic for the new instruction (to generate a binary with new instruction)
  Define the new instruction in SimX
  Extend the pipeline/decoder
  Modify the LSU to take in prefetch instructions
  Develop a test to check functionality of the new instruction
Debugging using kernel dump and run log
Already implemented in latest version of Vortex; use VM instead
Notes: 14

## Slide 15
Checking Solutions for Assignments #3 & #5
Check solutions folder on Github
  Solution overview and code provided
Download and execute solution
  Solution code formatted as git pull requests
  Assignment 3:
    git fetch origin pull/22/head:A3_solution git checkout A3_solution
  Assignment 5:
    git fetch origin pull/25/head:A5_solution git checkout A5_solution
Notes: 15

## Slide 16
Assignment 6
Add performance counters to test software prefetcher
Measure prefetch metrics
  # of unique prefetch requests
  # of unused prefetched blocks
  # of late prefetches
Part #1: extending the cache tag
Part #2: extending bank.sv to keep track of the meta data
Notes: 16

## Slide 17
Thank you
https://github.com/vortexgpgpu/vortex_tutorials
Notes: 7