## Slide 1: Vortex Software Stack
Blaise Tine
Notes: Narration:
This poster presents Vortex, a reconfigurable and scalable RISC-V GPGPU accelerator.
Vortex’s main goal is to use RISC-V to utilize the advantages of SIMT execution model and provide a customizable design to facilitate architecture research.
In addition, we show that a minimal set of 5 instructions is enough to achieve a highly parallel execution model on RISC-V.
Single Instruction Multiple Threads execution model, or SIMT, has the advantage of having a scalar based programming model, which makes it easier to program on.
Through POCL, an open-source framework to implement the compiler and runtime software for OpenCL, we were able to execute unmodified OpenCL kernels on Vortex.
We achieved that by linking POCL with Vortex's runtime kernel, which provides warp and thread creation, warp barriers, and control divergence.
Vortex microarchitecture has two main configuration methods to scale for various application domains: increasing the number of parallel work-items and configuring the cache system. Each one of these methods has its own unique trade-offs, both in terms of performance for different applications and hardware and energy cost. The first method is to increase the parallel work-items in the design by either increasing the number of threads per warp, number of warps per core, number of cores per clusters, and the number of clusters. The second method is by configuring the cache system. Our L1, shared memory, L2, and L3 are all based on the same high-throughput banked design that supports a snoop protocol and prefetching.
We have evaluated our design both 15 nm educational library and Arria 10 Intel FPGA on a subset of Rhodina benchmarks and were able to achieve frequencies of 300 MHz and 192 MHz respectively.
In addition, we were able to fit a 2 cluster 8 core configuration with a total of 256 work units on Arria 10 Intel FPGA.
We also used the OPAE open-source accelerator API to be able to execute OpenCL kernels on the FPGA.

## Slide 2
Vortex Software Stack
PoCL for the Vortex
LLVM Compiler Extension
Agenda
Notes: The agenda looks like this.

## Slide 3
__kernel void foo(){
tid = get_global_id(0);
…
barrier(…);
}
__host int main(){
…
cl_mem A_clmem = clCreateBuffer(context, …); clEnqueueNDRangeKernel(command_queue, foo, …); …
}
GPU Application (OpenCL, CUDA … )
Software Support
Vortex GPU
CPU-GPU communication
Kernel threads scheduling
Kernel execution
GPU capabilities query
Kernel and host code compilation
GPU buffer allocation
Kernel scheduling and execution
Motivation
Notes: People use GPU programming languages to develop GPU applications.
Many individuals employ languages like OpenCL and CUDA for writing their applications, and numerous applications have already been developed using these languages.
These two languages divide the program into two parts: code for the kernel and code for the host.
Kernel code requires access to runtime information, such as global IDs in OpenCL or thread IDs in CUDA.
kernel code also requires controlling program flow, including barriers and terminating executions.
On the other hand, host code needs to establish communication with the Vortex GPU, specifying commands for actions such as kernel launches and memory allocation.
Therefore, we require two types of methods: the first for accessing runtime information and controlling program flow, and the second for communication with the device.
On the Vortex side, programs must be written in Vortex ISA, not RISCV or any other instruction set.
Runtime information is stored in their local control and status registers.
Vortex uses the opae driver to configure, enumerate, open, and access FPGA accelerators.
However, there remains a significant gap between the programmer's code and the access to runtime information and communication.

## Slide 4: Overview of the Vortex Software Stack
Supporting laungague
  OpenCL (v3.0)
  CUDA (v10.1)
Frontend compiler
  Portable Computing Language (PoCL)
    Extension of PoCL v5.0
  Cuda for Parallelized and Broad-range Processors(CuPBoP)
Common Component
  RISCV toolchain (gcc, build_utils, etc)
  LLVM vortex
    Extension of LLVM 18
CuPBoP
Vortex Binary
vortex
Open-GPU owned
repositories
Modified repositories
Notes: The Vortex software stack provides support for two different programming languages: OpenCL and CUDA. Currently, we offer support for OpenCL 3.0 and CUDA 10.1.
To enable support for these two languages, we use the Portable Computing Language (PoCL) and CUDA for Parallelized and Broad-range Processors.
We have extended the PoCL open-source repositories to ensure compatibility with Vortex and have implemented our own project called CupBoP.
As our backend compiler, we utilize LLVM, specifically an extended version 16. To fully support the entire software stack, we also require the RISC-V toolchain, which includes essential components such as GCC and various build utilities. These components are integral to our comprehensive software stack.

## Slide 5
GPU Kernel
Kernel Compilation Stack
Vortex Kernel library
Target Codegen Compiler
Vortex Host Program
Program Execution Stack
Language-specific Runtime library
Vortex Runtime library
Language-specific Compiler
Vortex Kernel & Runtime Stacks
Notes: To bridge the gap between the GPU and the code, we have implemented a software stack.
This is the Overview of the vortex software stack, which comprises two distinct components: kernel compilation into the Vortex binary and program execution.
The GPU kernel is defined using languages such as OpenCL or CUDA.
Our process begins with the analysis of program semantics and the generation of intermediate representation (IR) for the program.
Subsequently, we link with libraries that contain pre-built kernels for accessing runtime information and controlling program flow.
Lastly, we generate target code that consists of Vortex ISA instructions.
The program execution stack is also defined by specific programming languages.
In this case, we link function calls to methods that align with Vortex operations, such as Vortex memory allocation.
The Vortex runtime library contains essential information for communicating with the Vortex hardware.

## Slide 6: Vortex ISA Extension
  Wavefront Activation
    vx_wspawn %numW %func_ptr
  Thread mask activation and Active thread modification
    vx_tmc %tmask, vx_pred %cond %tmask
  Control flow divergence and reconvergence
    vx_split %pred, vx_join %stack_ptr
  Wavefront synchronization
    vx_barrier %barID %numW
A
B
C
D
If (threadid.x<2) {
work B
} else {
work C
}
Example Kernel
Control Flow Graph
Start
vx_join
vx_wspawn
vx_split
vx_join
Notes: Now, I will provide a more detailed introduction to the libraries and ISA extensions of the Vortex.
In order to support GPU operations, we have extended the RISCV ISA.
Since GPUs follow a SIMT (Single Instruction, Multiple Threads) architecture, it is important to have an ISA that can effectively control operations in SIMT architecture.
vortex use terminology wavefront and thread.
A wavefront is a group of thread and threads within one wavefront are executed in parallel and in lock steps.
The Vortex ISA introduces instructions for wavefront activation, allowing the launch of a kernel across a specified number of warps with a function pointer.
To manage threads within a warp, we introduce two ISAs, namely vx_tmc and vx_thread. These ISAs are responsible for activating and altering the active threads.
One of the most important aspects of the Vortex ISA is the introduction of split and join instructions to handle control divergence.
For instance, consider the code snippet in the top-right corner, which executes "work b" when the thread ID is greater than 2, otherwise, it runs "work c."
This code can lead to control flow divergence like bottom right figure.
To address control flow divergence in vortex, the split instruction pushes information about the current state of the thread mask into a hardware-immediate post-dominator (IPDOM) stack.
Subsequently, the join instruction retrieves this information during reconvergence.
Additionally, we have incorporated instructions for synchronization purposes.

## Slide 7: Vortex Kernel Library
Interface for accessing runtime information and controlling program flow
  Schedule tasks on the parallel H/W
    void vx_spawn_threads(dimension, grid_dim, block_dim, kernel_func, arg)
  Query hardware configuration
    vx_num_cores(), vx_num_warps(), vx_num_threads()
  Query the current thread or wavefront
    vx_thread_tid(), vx_warp_id()
  Terminate program execution
    vx_tmc();
  Debug print to the console
    vx_printf(format, …);
  Other utility APIs
Notes: The Vortex kernel libraries consist of a set of kernels designed for running applications on the Vortex hardware.
In order to retrieve information and query hardware status, we require an interface, called vortex kernel library.
This vortex kernel library needs to be provided during kernel compilation.

## Slide 8: Vortex Runtime Library
Interface for communicating with the Vortex device
  Perform memory-related operation?
    vx_mem_alloc(…), vx_mem_free(…)
    vx_copy_to_dev(…), vx_copy_from_dev(…)
  Launch Kernel?
    vx_start(…), vx_ready_wait(…)
  Open and Close Device?
    vx_dev_open(…), vx_dev_close(…)
  Other Runtime Methods
Notes: For host code, certain fundamental operations must be implemented for communicating vortex and host CPU.
These operations include memory copying, memory allocation, and kernel launching, and all of these functions should be incorporated into the Vortex Runtime library.

## Slide 9
Kernel Code
(IR)
Built-in Library
(e,g. math functions)
Kernel executable
Vortex ISA
Front-end compiler
Back-end compiler
Analyze program semantics
Lower functions with built-in library
Lower IR to Vortex ISA using Vortex intrinsic
Perform vortex-specific optimization
Vortex
Kernel library
Host
Executable
Compiler
Lower device communication functions with runtime library
Vortex Runtime
Host Code
Kernel Code
Vortex Program Compilation Flow
Notes: Now, I would like to provide a more detailed explanation of the Vortex compilation flow.
Compiler receive kernel code and host code as a input of compiler pipeline.
The kernel code undergoes initial analysis of program semantics through the front-end compiler, resulting in the generation of intermediate representation (IR). During this process, some functions are lowered using built-in libraries is performed.
Subsequently, the generated IR is transformed into a kernel executable by the backend compiler.
In this phase, the Vortex ISA is employed, and the Vortex Kernel library is linked.
On the other hand, the host code is responsible for creating the host executable through linkage with the runtime library.

## Slide 10
Front-end runtime library
Vortex Runtime Library
Vortex Host interface
Command Processor
Vortex Processor
External
Bus
Internal
Bus
Host
Vortex GPU
Vortex Execution flow
Notes: Now I will introduce the Vortex execution flow.
The commands required for device communication, as outlined in the host code, adhere to the following execution sequence:
First, they are linked with the frontend runtime library.
The frontend runtime library outlines how frontend methods can be executed using the Vortex runtime library.
The Vortex library carries out the operation using the Vortex host interface.
Vortex host interface, in turn, performs the operation on the Vortex processor, which is connected to the external bus via the Vortex host interface.

## Slide 11: Vortex OpenCL System Architecture
Compilation
  Vortex Kernel Library
  PoCL Compiler
Execution
  Vortex Runtime
  PoCL Runtime
Vortex Runtime
Vortex Kernel
Notes: The vortex PoCL extension make available compile OpenCL kernel and execute them in the vortex GPU.
we need to care about the following parts: for compilation, we need to modify the POCL Compiler and provide a Vortex Runtime library.
For the Compilation, vortex have different interface as other devices.
thus, we have to modify the original pocl compiler to generate the programs with Vortex ISA.
We also use vortex kernel library in lowering process.
For execution, we need to provide a Vortex runtime for POCL runtime. To integrate a new device into POCL, we have to implement some basic operations, like memory copy, memory allocation and kernel launch and put all these functions into Vortex Runtime. POCL framework will use the Vortex Runitme to control and communicate with Vortex.

## Slide 12
Thank You!
https://github.com/vortexgpgpu/pocl/tree/main
https://github.com/vortexgpgpu/llvm/tree/vortex
https://github.com/vortexgpgpu/vortex