## Slide 1: GPGPU Background
Hyesoon Kim

## Slide 2: GPU pipeline
Warp/Wave-front execution model
SPMD programming model (Single Program Multiple Data)
Inst 1
Inst 2
Inst 3
T1
Inst 1
Inst 2
Inst 3
T2
T3
T4
All threads have the same program
T
T
T
T
One warp
T
T
T
T
Fetch 1 instruction and each instruction has multiple threads are associated.
The group of instruction is called warp/wave-front
Tn
…
T
T
T
T
One warp
T
T
T
T

## Slide 3: Execution Model
Thread & Block
Inst 1
Inst 2
Inst 3
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
SM
SM
Shared Memory
SP
SP
SP
SP
Shared Memory
SP
SP
SP
SP
Block
Kernel
Block
warp
warp
warp
Sing instruction multiple thread
Block = a group of thread which share “the shared memory space”
Warp
warp
warp
warp
[the slide is from Hong&Kim ISCA’09]

## Slide 4: Memory Data Indexing
SIMT-execution model
Use thread id and block id to index data
Let’s assume N=16, blockDim=4  4 blocks
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
blockIdx.x = 0
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 0,1,2,3
blockIdx.x = 1
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 4,5,6,7
+
blockIdx.x = 2
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 8,9,10,11
blockIdx.x = 3
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 12,13,14,15
+
+
+
+

## Slide 5: 1D, 2D, 3D data structures
A kernel is executed as a grid of thread blocks
Threads and blocks have IDs
  So each thread can decide what data to work on
  Block ID: 1D or 2D
  Thread ID: 1D, 2D, or 3D
Loop index in sequential loop
  Use thread ids, block ids
  1D array index= c1*threadId.x + c2*block Id.x
  2D array index = c1*threadId.x+c2*blockId.x+c3*threadId.y+c4*blockId.y
for (ii = 0; ii < 100; ++ii) {
C[ii] = A[ii] + B[ii];
}
// there are 100 threads
__global__ void KernelFunction(…) {
int tid = blockDim.x * blockIdx.x + threadIdx.x;
int varA = aa[tid];
int varB = bb[tid];
C[tid] = varA + varB;
}
CPU code
CUDA code

## Slide 6: CUDA Program Example

## Slide 7: OpenCL vs. CUDA
 | OpenCL | CUDA
Execution Model | Work-groups/work-items | Block/Thread
Memory model | Global/constant/local/private | Global/constant/shared/local + Texture
Memory consistency | Weak consistency | Weak consistency
Synchronization | Synchronization using a work-group barrier (between work-items) | Using synch_threads Between threads

## Slide 8: GPU Pipeline
Fetch
  One instruction for each warp
  Multiple PC registers exist to support multi-threaded architecture
  Round-robin scheduler
Wide execution width
Scheduler
I-cache
Fetch unit
Decoder
. . . . . .
Memory access unit
. . . . . .
Writeback
Memory
Lane 0
Lane 1
Lane N-1
Lane 0
Lane 1
Lane N-1
Active bit mask vectors/
score boarding
Register
Scheduler (Score boarding)

## Slide 9: Handling Branch Instructions
A reduction example
What about other threads?
What about different paths?
0
1
2
3
4
5
6
7
0
2
4
6
0
4
0
If (threadId.x%==2)
If (threadId.x%==4)
If (threadId.x%==8)
A
B
C
D
If (threadid.x>2) {
do work B}
else {
do work C
}
From Fung et al. MICRO ‘07
Divergent branch!

## Slide 10: Split/Join
Compiler inserts split/join
Split:
  Put tmask in the ipdom stack (do work c part}
  Put next PC in the stack (not-taken path. // do work c part )
Join
  Pop from a stack
If (threadid.x>2)
// split
{
do work B
}
else {
// join
do work C
}

## Slide 11: GPU Pipeline (1)
 | PC value
#1 (b:1, T1-T4) | 0x8000
#2 (b:1, T5-T8) | 0x8004
#3 (b:2, T1-T4) | 0x8000
#4 (b:2, T5-T8) | 0x800A
I-cache
Front-end
Decode
Memory
RF
Execution
Write-back
schedule
Shared Memory
0x8000 | add r1, r1, 1
0x8004 | sub r2, r,2,1
0x8008 | mov r1, tid.x
0x800A | mov r2, ctaid.x
0x8010 | ld.shared r1 [A]
tid.x: special register to store thread ID within a block
ctaid.x: special register to store block ID within a grid
 | Th1 | Th2 | Th3 | Th4
R1 | 11 | 12 | 13 | 14
R2 | 2 | 2 | 2 | 2
R3 | 3 | 4 | 13 | 15
R4 | 23 | 24 | 32 | 33
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
1
1
1
1
11
12
13
14
12
13
14
15
add r1, r1, 1
add r1, r1, 1
add r1, r1, 1
add r1, r1, 1
add r1, r1, 1
add r1, r1, 1

## Slide 12: GPU Pipeline (2)
 | PC value
#1 (b:1, T1-T4) | 0x8000
#2 (b:1, T5-T8) | 0x8004
#3 (b:2, T1-T4) | 0x8000
#4 (b:2, T5-T8) | 0x800A
I-cache
Front-end
Decode
Memory
RF
Execution
Write-back
schedule
Shared Memory
0x8000 | add r1, r1, 1
0x8004 | sub r2, r,2,1
0x8008 | mov r1, tid.x
0x800A | mov r2, ctaid.x
0x8010 | ld.shared r1 [A]
tid.x: special register to store thread ID within a block
ctaid.x: special register to store block ID within a grid
 | Th1 | Th2 | Th3 | Th4 | Th5 | Th6 | Th7 | Th8
R1 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
R2 | 3 | 3 | 3 | 3 | 2 | 2 | 2 | 2
R3 | 3 | 4 | 13 | 15 | 23 | 32 | 37 | 23
R4 | 23 | 24 | 32 | 33 | 11 | 7 | 8 | 5
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
1
1
1
1
2
2
2
sub r2, r2, 1
1
1
1
sub r2, r2, 1
sub r2, r2, 1
sub r2, r2, 1
sub r2, r2, 1
One lane is not shown

## Slide 13: Mask Bits
What if we do not need to execute all 4 threads?
Mask bits tell which threads are active.
 | Src 1 |  | Src 2 | 
w1 | v | r | v | r
w2 | v | r | v | r
w3 | v | r | v | r
w4 | v | r | v | r
w5 | v | r | v | r
 | Src 1 |  | Src 2 | 
w1 | v | r | v | r
w2 | v | r | v | r
w3 | v | r | v | r
w4 | v | r | v | r
w5 | v | r | v | r
 | Src 1 |  | Src 2 | 
w1 | v | r | v | r
w2 | v | r | v | r
w3 | v | r | v | r
w4 | v | r | v | r
w5 | v | r | v | r
 | Src 1 |  | Src 2 | 
w1 | v | r | v | r
w2 | v | r | v | r
w3 | v | r | v | r
w4 | v | r | v | r
w5 | v | r | v | r
V
V
V
V
V
V
V
V
id | Mask bit
w1 | 1111
w2 | 1110
w3 | 0111
w4 | 1111
w5 | 1111
V
V
V
V
V
V
V
V
V
V

## Slide 14: Summary
GPUs execute many threads as a group (warp/wave front)
GPU provides features to handle multiple threads concurrently and also time multiplexing
Massive thread level parallelism  massive memory level parallelism

## Slide 15: A few links:
Tutorial Homepage:
https://github.com/vortexgpgpu/vortex_tutorials/
https://github.com/vortexgpgpu/vortex_tutorials/blob/main/REMOTE_ACCESS.md
Please use the form to submit your Github ID to reserve a slot to use for the duration of the tutorial