## Slide 1: Vortex 3.0 Software Stack
Blaise Tine
MICRO-59 Tutorial · November 2026

## Slide 2: Agenda
  The stack: front ends, compiler, runtime, backends
  ISA surface and kernel-side intrinsics
  Runtime: host–device flow, vortex2.h, barriers, tensor API
  OpenCL (PoCL 7), HIP (chipStar), Vulkan (vortexpipe)
  Build configuration and simulation vehicles
  CI: parity, perf, FPGA and ASIC gates; Perfetto
  Writing and debugging a native program

## Slide 3: The Software Stack in One Picture
Versions
  LLVM 20 · POCL 7.0 · chipStar (vortex_3.x) · Mesa (lavapipe + vortexpipe) · CuPBoP (CUDA 12.1)
Install shape
  make install → $VORTEX_PATH/{kernel,runtime}/{include,lib<XLEN>} + vortex-{runtime,kernel}.pc; downstream links only the install tree
OpenCL C / SPIR-V
HIP (hipcc)
CUDA (nvcc-like)
Vulkan (GLSL / SPIR-V)
Native C/C++ (vx_*)
PoCL 7.0 — Vortex device driver
chipStar → SPIR-V
CuPBoP-Vortex
lavapipe → vortexpipe (NIR → LLVM IR)
clang direct
VOLT compiler — LLVM 20 + Vortex SIMT backend (+xvortex, +zicond) → riscv{32,64} ELF → vxbin.py → .vxbin (details: next talk)
Device: sw/kernel — vx_intrinsics.h, vx_spawn2.h, vx_tensor.h, vx_dxa.h, vx_barrier.h, vx_graphics.h, vx_print.h → libvortex2.a
Host: sw/runtime — vortex2.h (queues, events, modules, kernels, UVA args) + dxa.h / graphics.h / tensor.h → libvortex.so
libvortex-simx
-rtlsim
-xrt
-opae
-aved
-gem5
-firesim
VORTEX_DRIVER selects the backend at load time (sw/runtime/stub)
Notes: Last year: OpenCL (PoCL 5) and CUDA (CuPBoP) on LLVM 18. This year: PoCL 7.0 carries OpenCL C, SPIR-V and HIP (through chipStar); Mesa vortexpipe carries Vulkan; CuPBoP still carries CUDA. All feed VOLT (LLVM 20 with the Vortex SIMT backend) and link the device runtime libvortex2.a. On the host, every front end calls the same vortex2.h API from the SDK install tree; libvortex.so is a stub that loads the backend named by VORTEX_DRIVER.

## Slide 4: ISA Surface in v3.0
MISA feature bits
  TEX = 6, RASTER = 7, OM = 8, TCU = 9, DXA = 10
  Queried by software via VX_CAPS_ISA_FLAGS
Async barriers
  arrive / wait(phase) / expect_tx on the bar unit
  bar id = {index << 8 | CTA slot}; group and global forms
Design rule for accelerators
  per-dispatch → DCR; per-warp → lane packing (vx_wgather)
  per-thread → register window; bulk → custom load
Standard extension | v3.0 status
I / M / F (RV32, RV64) | baseline
D (double) | native F64 in VX_fpu_std (XLEN=64)
A (atomics) | LR/SC + 9 AMO ops, Zacas optional
C (compressed) | VX_decompressor in fetch stage
Zicond | CZERO.EQZ / CZERO.NEZ
M-mode traps | ECALL / EBREAK / MRET + 6 CSRs
Vortex custom opcode space | Contents
custom-0 (0x0B), by funct7 | 0x00 warp ctl (tmc, wspawn, split, join, bar, pred, wsync) · 0x01 vote/shuffle · 0x02 tensor · 0x03 DXA · 0x04 pack-load
custom-1 (0x2B), by funct3 | 0 vx_wgather · 3 vx_om_export · 5 vx_tex · 6 RTU hit window · 7 vx_rt_trace / vx_rt_wait
custom-2 (0x5B) | MUFU: rcp, rsqrt, ex2, lg2, sinpi, cospi, tanh
Notes: Standard RISC-V extensions now implemented in hardware: A (LR/SC + AMO*, completed at the LLC), C (decompressor in fetch), Zicond, F and D. Vortex custom instructions live in custom-0 (by funct7) and custom-1 (by funct3); MUFU transcendental ops in custom-2. MISA advertises TEX=6, RASTER=7, OM=8, TCU=9, DXA=10 so software can query the device.

## Slide 5: Kernel Side: ISA Intrinsics and vx_spawn2
vx_spawn2.h
  __kernel = vortex.kernel calling convention: no callee-saved spills, ra saved
  blockIdx / blockDim / gridDim / threadIdx read CTA CSRs 0xCD0–0xCE1
  KMU dispatches CTAs; __vx_cta_entry prologue runs once per CTA, then vx_tmc zero
Also in sw/kernel
  vx_print.h (vx_printf via host console), vx_barrier.h, vx_dxa.h, vx_tensor.h, vx_graphics.h
  libvortex2.a: startup (vx_start.S), KMU entry, printf, newlib glue
Intrinsic | Instruction / effect
vx_wspawn(n, pc) | activate n warps at pc
vx_tmc(mask) · vx_pred(c, mask) | thread mask control · predication
vx_split(p) / vx_join(sp) | IPDOM push / pop (compiler-inserted)
vx_barrier(id, n) · vx_barrier_arrive / _wait / _expect_tx | synchronous and split barriers (VX_bar_unit)
vx_wgather(a0..a3) | pack 4 scalars of one lane into 4 lanes (R4)
vx_vote / vx_shuffle / vx_quad_ddx | custom-0 funct7 0x01 cross-lane ops
vx_packlb_f / vx_packlh_f | strided pack-loads (4 LSU uops)
vx_dxa_issue_{1..5}d_wg, _multicast_wg | DXA copy (custom-0 funct7 0x03)
vx_tensor.h: wmma / wgmma / TCU_LD | tensor ops (funct7 0x02)
vx_rt_wtrace / wait / continue · vx_tex · vx_om_export | custom-1 graphics / RT
vx_rsqrt, vx_ex2, … | MUFU (custom-2)
#include <vx_spawn2.h>
struct kargs { float *a, *b, *c; uint32_t n; };
__kernel void vecadd(kargs *k) { // vortex.kernel CC
uint32_t tid = blockIdx.x * blockDim.x + threadIdx.x;
if (tid < k->n) k->c[tid] = k->a[tid] + k->b[tid];
}
// CSR-backed ids: VX_CSR_CTA_THREAD_ID_X,
// CTA_BLOCK_ID_*, CTA_BLOCK_DIM_*, CTA_GRID_DIM_*
Notes: The warp-control intrinsics are unchanged in spirit — wspawn, tmc, split/join, pred, barrier — plus the v3 additions: split barriers, DXA issue, tensor, RT, pack-loads, vote/shuffle, wgather. The kernel-library entry point is now vx_spawn2.h with the vortex.kernel calling convention and the CTA CSR family for ids and dimensions.

## Slide 6: Program Compilation Flow (v3.0)
Kernel code
Kernel source (OpenCL C / SPIR-V / HIP / CUDA / C++)
Front end (PoCL · chipStar · CuPBoP · clang) → LLVM IR
llvm-link: builtins (kernel-riscv{32,64}.bc), work-group passes, processKernels wrapper
VOLT compiler: RISC-V + Vortex ISA codegen (next talk)
ld: libvortex2.a + newlib libc.a, --gc-sections, 16 MB code base (112 module slots)
vxbin.py → .vxbin [min_vma | max_vma | image | VXSYMTAB]
Host code
Host source (vortex2.h, or OpenCL / HIP / Vulkan API)
host compiler (gcc / clang) + translator runtime (libpocl, libCHIP, mesa)
link libvortex.so via pkg-config --libs vortex-runtime
runtime: vx_module_load_file(.vxbin) → vx_module_get_kernel(name)
cc main.cpp $(pkg-config --cflags --libs vortex-runtime)
VORTEX_DRIVER=simx ./main # or rtlsim | xrt | opae
./ci/blackbox.sh --driver=rtlsim --app=vecadd --debug=3
Notes: Same two-sided picture as last year with the v3 pieces named. Kernel: front end → IR → link builtins and the per-XLEN kernel bitcode → VOLT passes → Vortex ISA → ELF linked at a 16 MB code base with libvortex2.a and newlib → vxbin.py (symbol table footer). Host: the application compiles against vortex2.h and links libvortex.so from the SDK; a .vxbin is loaded with vx_module_load_file and kernels resolved by name.

## Slide 7: Host–Device Execution Flow
Host
Application (OpenCL / HIP / Vulkan / native)
PoCL · chipStar · vortexpipe
vortex2.h: vx_enqueue_launch / vx_enqueue_memcpy …
per-queue worker thread → encode command (64 B line)
memcpy into ring + doorbell (Q_TAIL)
Vortex device
Command Processor
fetch → unpack → engine → arbiters
KMU launch
DMA
DCR proxy
Event unit
Cache flush
KMU: grid walk → launch-bus tree → per-core CTA dispatchers
Cores run warps; busy falls → CMD_LAUNCH retires → seqnum written to host
Device memory
(DMA via axi_dev)
ring
fetch
+
seqnum
A launch = 20× CMD_DCR_WRITE + CMD_LAUNCH + CMD_CACHE_FLUSH. Host cost per command: one memcpy + one doorbell; everything else is device work.
Notes: In v2 the host poked DCRs and a start register directly. In v3 every host action is a command in a host-resident ring: memory writes/reads, DCR writes, launches, cache flushes, events. The CP fetches commands over its host AXI port, drives the KMU, and writes a completion sequence number back. The same CP model (C++) runs under SimX, rtlsim and gem5; RTL CP runs on FPGA.

## Slide 8: VortexRT: the vortex2.h Runtime API
Shape-lock features
  timeline events: host-side refcounted, monotonic counter + condvar; vx_event_{signal,get_value,wait_value,wait_values,get_profiling}
  module / kernel handles from .vxbin + VXSYMTAB; legacy → "main"
  UVA raw-pointer args: runtime stages the blob into a per-device scratch slot and programs KMU ARG DCRs
Execution
  each vx_enqueue_* pushes a lambda to a per-queue worker thread
  batch: vx_enqueue_commands = one doorbell (used for TEX binds + launch)
Deferred (additive)
  pools, indirect dispatch, host functions, SVM, command buffers, per-arg setters
  escape hatch: kernel == NULL, args_host == NULL, ndim == 0 → pre-programmed DCRs
vx_device_h
vx_buffer_h
vx_queue_h
vx_event_h
vx_module_h
vx_kernel_h
vx_dev_open(0, &dev); vx_mem_alloc(dev, N, VX_MEM_READ_WRITE, &buf);
vx_queue_create(dev, &q);
vx_module_load_file(dev, "kernel.vxbin", &mod);
vx_module_get_kernel(mod, "add_k", &kernel);
vx_launch_info_t li = { .kernel = kernel,
.args_host = &args, .args_size = sizeof(args),
.ndim = 1, .grid_dim = {G}, .block_dim = {B},
.cluster_dim = {1, 1, 1} };
vx_enqueue_memcpy_htod(q, buf, src, N, 0, &ev0);
vx_enqueue_launch(q, &li, &ev1);
vx_enqueue_memcpy_dtoh(q, dst, buf, N, 0, &ev2);
vx_event_wait_value(ev2, 1); // timeline
Notes: A locked v1 core in the shape of Vulkan/CUDA runtimes: six opaque handles, queues, timeline events, modules and kernels, raw-pointer UVA kernel arguments. Complexity is pushed up to the translators (PoCL, chipStar, vortexpipe) and sideways into per-block helpers (dxa.h, graphics.h, tensor.h). The legacy vortex.h survives as a thin wrapper.

## Slide 9: Asynchronous Barriers: ISA and Kernel API
Barrier id packing
  barrier: (index << 8) + local group id (CTA slot) → rows isolated per CTA
  gbarrier: (index << 8) | 0x80000000 → cluster-level unit, counts cores
  group_barrier: (index << 8), no CTA id → all K members share one row
Configuration
  VX_CFG_NUM_BARRIERS = 8 per CTA · VX_CFG_MAX_BAR_EVENTS = 32
  bar unit row = {warp mask, count, events, phase}
Why
  producer announces a tile and moves on; consumers wait on one phase
  engines complete barriers directly — no polling warp, no shared-memory object
Primitive | Semantics
arrive(bar, count) | count the warp; returns phase bit sampled before arrival
wait(bar, phase) | stall while barrier phase == phase (one bit flips per generation)
expect_tx(bar, n) | add n pending completion events (cumulative)
arrive_and_wait | fused = legacy bar id, count (BAR drains the LSU first)
engine completion | DXA last-line write → VX_dxa_completion → txbar → events−1
vortex::barrier bar(0, num_warps); // id<<8 | CTA slot
bar.expect_tx(1); // one DXA transfer
vx_dxa_issue_2d_wg(smem, desc, x, y, bar.id());
... compute on the previous tile ...
uint32_t ph = bar.arrive(); // non-blocking
bar.wait(ph); // tile landed
vortex::gbarrier g(1, vx_num_cores()); // cores
vortex::group_barrier gb(2, K); // co-resident CTAs
Notes: The scheduler barrier became a split, transaction-aware barrier: arrive counts the warp and returns the phase bit; wait blocks while the phase still equals the one observed; expect_tx pre-registers pending transaction events that asynchronous engines complete — DXA posts one completion per transfer into the barrier named at issue. A fused arrive-and-wait with no events is the old synchronous barrier, so existing kernels run unchanged. Three kernel-side classes: barrier (CTA), gbarrier (cores), group_barrier (co-resident CTAs).

## Slide 10: Tensor API: vx_tensor.h
Compile-time selection
  ITYPE / OTYPE, NRC ∈ {8, 16, 32}, RS vs SS; wgmma_config_t + wgmma_context
  same source → dense WMMA, dense WGMMA, sparse WGMMA
Host helpers
  prune_2to4_matrix → compress_2to4_matrix → pack_metadata_wg
  vortex::dxa::program_{1..5}d descriptors for tile staging
Kernel helpers
  load_matrix_sync (RS), vx_make_smem_desc (SS), load_sp_metadata, wgmma_sync, store_matrix_sync
  A section per warp padded to a bank row so warp w+1 starts on a fresh row
Where it lives
  sw/kernel/include/vx_tensor.h · sw/common/tensor_cfg.h (ABI, installed)
#include <vx_tensor.h>
using ctx = vortex::tensor::wgmma_context<
fp16 /*ITYPE*/, fp32 /*OTYPE*/, NRC, Mode::SS>;
ctx::fragment_acc C; ctx::fill_fragment(C, 0);
for (k = 0; k < K; k += ctx::tileK) {
// stage A, B into shared memory (loads or DXA)
auto dA = vx_make_smem_desc(A_smem, strideA);
auto dB = vx_make_smem_desc(B_smem, strideB);
ctx::load_sp_metadata(fragA, meta); // 2:4 only
ctx::wgmma_sync(C, dA, dB, C); // SS mode
}
ctx::store_matrix_sync(pC, C, N);
Notes: Same shape as last year, now with WGMMA and sparsity selected at compile time: input/output format, accumulator count NRC and RS-vs-SS mode are template parameters, so one kernel source compiles to dense WMMA, dense WGMMA or sparse WGMMA. The host side prunes and compresses A and packs the 2:4 metadata into the per-thread SRAM layout the TCU_LD expects.

## Slide 11: OpenCL on Vortex: PoCL 7.0 System Architecture
Ownership
  external: vortexgpgpu/pocl @ vortex_3.x (driver, builtin library) → $TOOLDIR/pocl
  in-tree: tests/opencl (48 apps + Rodinia + common.mk), ci/testcases/opencl.yaml, sw/kernel → libvortex2.a
Driver
  pocl-vortex.c: pocl_device_ops, caps, build, pocl_vortex_run, buffers / images, async worker
  vortex_utils.cc: processKernels (argument-buffer wrapper, vortex-kernel attribute, verifyModule), compile_vortex_program
Async model
  submit → ready_list / command_list; worker pocl_vortex_driver_thread runs pocl_exec_command off the caller's stack
  why: inline execution re-enters the buffer lock (pocl_free_event_memobjs) → self-deadlock
Config threading
  common.mk: POCL_VORTEX_XLEN / _CFLAGS / _LDFLAGS / _BINTOOL
OpenCL application (-lOpenCL)
ocl-icd loader → Vortex .icd (OCL_ICD_VENDORS pinned)
libpocl.so (ICD-only): core + Vortex device driver
pocl-vortex.c · vortex_utils.cc
libvortex.so stub → VORTEX_DRIVER
libvortex-{simx, rtlsim, xrt, opae}.so
Notes: The host links the system ocl-icd loader; PoCL is built ICD-only with the Vortex device driver statically linked into libpocl.so — the only code that issues vx_* calls. The driver is two files: pocl-vortex.c (ops table, run, async worker) and vortex_utils.cc (processKernels, JIT). The device ISA is queried once and validated against what the driver emits. clEnqueue* is asynchronous: submit pushes to a ready list and a worker thread executes off the caller's stack — a correctness requirement, because PoCL submits migrations while holding a buffer lock.

## Slide 12: OpenCL: JIT Pipeline, Launch and Memory Model
Launch
  __local args aligned to VX_LOCAL_ALIGN = 128 B; vx_enqueue_launch; TEX DCR writes + launch in one vx_enqueue_commands batch
Rules
  "true-GPU rule": add a missing capability to Vortex, never emulate it in PoCL; .bc not self-contained so missing builtins fail at link; verifyModule on (PoCL disables it)
  CTS runs serially on SimX (functional MT kernel)
front end: Clang (OpenCL C) or spirv_parser (SPIR-V) → LLVM IR; target riscv{32,64} +xvortex +zicond, no RVV
llvm-link with kernel-riscv{32,64}.bc (builtin library)
PoCL work-group passes
processKernels: argument-buffer wrapper, vortex-kernel attribute, .callee clone, verifyModule
codegen + ELF link (libvortex2.a, newlib libc.a, --gc-sections, 16 MB base) → vxbin.py
vx_module_load_file → code slot (112 × 16 MB below 0xF0000000)
Capability (CL_DEVICE_*) | Vortex 3.0
profile / version | FULL_PROFILE, OpenCL 1.2 (PoCL 7.0 core)
MAX_WORK_GROUP_SIZE | num_warps × num_threads (one CTA, one core)
int64 | core (soft on rv32)
atomics (int32) | gated on A extension (VX_ISA_EXT_A)
images | software; FF 2D fast path via TEX (VX_ISA_EXT_TEX)
fp64 / fp16 | not advertised
MAX_MEM_ALLOC_SIZE | max(global / 4, 128 MB)
MAX_CONSTANT_BUFFER_SIZE | 64 KB
Notes: clBuildProgram runs the PoCL pipeline then the Vortex post-build hook: front end (Clang or spirv_parser) with target riscv{32,64} +xvortex +zicond, llvm-link against the per-XLEN kernel bitcode, work-group passes, processKernels, codegen and ELF link, vxbin.py, vx_module_load_file into one of 112 16 MB code slots. Launch: __local arguments aligned to 128 bytes, a work-group is one CTA and never spans cores, max work-group size = warps × threads; TEX binds for images are folded into one command batch with the launch.

## Slide 13: HIP on Vortex via chipStar (rv32 + rv64)
In-tree vs external
  in-tree: tests/hip (vecadd, sgemm, histogram, atomicreduce), common.mk, ci/chipstar_install.sh.in, hip.yaml
  external in $TOOLDIR: chipStar @ vortex_3.x (hipcc, libCHIP.so, hipspv-spirv{32,64}.bc), llvm_vortex, pocl
rv32 enablement
  Clang HIPSPV accepts spirv32 (Driver.cpp, HIPSPV.cpp); multi-width device library (HIPCC + ROCm-Device-Libs patches)
  POCL on rv32 accepts Physical32 SPIR-V (address_bits = 32)
Status
  vecadd / sgemm pass on rv32 SimX; chipStar conformance smoke ~36% passing on rv32 (known-failures-vortex32.txt)
  atomics: atomicAdd → amoadd.w; histogram / atomicreduce need -DVX_CFG_EXT_A_ENABLE
Not built (by design)
  native HIPVortex Clang driver, libhip_vortex (hipMalloc → vx_mem_alloc, no JIT), vortex_mlir — motivation: expose WMMA / WGMMA / DXA intrinsics the SPIR-V path cannot reach
HIP source
__global__, <<<>>>
hipcc (chipStar, CHIP_BE=opencl)
--offload-pointer-width={32,64}
SPIR-V
OpMemoryModel Physical32 / 64
PoCL spirv_parser → LLVM IR
→ VOLT JIT → .vxbin
libCHIP.so (both widths)
+ libvortex.so
simx · rtlsim · opae · xrt
__global__ void vecadd(const float *a, const float *b,
float *c, int n) {
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < n) c[i] = a[i] + b[i];
}
hipMalloc(&dA, n * 4); hipMemcpy(dA, hA, n * 4, hipMemcpyHostToDevice);
vecadd<<<grid, block>>>(dA, dB, dC, n);
hipDeviceSynchronize();
make -C tests/hip run-simx (passes --offload-pointer-width=$(XLEN), POCL_VORTEX_XLEN=$(XLEN))
pytest ci -m hip · ./ci/regression.sh --test hip (xlen: [32, 64], tier: smoke)
Accepted risk: POD-argument width drift (host size_t = 8 vs device 4 on rv32)
Notes: hipcc with CHIP_BE=opencl emits SPIR-V; PoCL's spirv_parser turns it into LLVM IR and JITs it to .vxbin, so HIP rides the same driver and device runtime as OpenCL. v3 added rv32: hipcc accepts --offload-pointer-width={32,64} and emits OpMemoryModel Physical32/64; a single libCHIP.so ships both widths' device libraries and picks at runtime from CL_DEVICE_ADDRESS_BITS. Vortex's own tree is untouched — the load-bearing pieces are external forks installed into $TOOLDIR. Four HIP tests run per driver at both XLENs; atomics tests need the A extension.

## Slide 14: Vulkan: the vortexpipe Gallium Driver
Layering
  Vulkan app → lavapipe ICD → Gallium pipe_screen / pipe_context → vortexpipe (overridden slots) → llvmpipe fallback
  device via $VORTEX_PATH SDK: libvortex.so / vortex2.h; one-directional mesa → Vortex dependency
vp_screen / vp_context
  vx_device_open once; caps hw_num_threads / warps / max_block_size / isa_flags, has_tex / raster / om / rtu
  residency table {host_base, size, buf, dev_addr, dirty} — dirty starts true so untaught paths re-upload
  per-CSO: llvmpipe CSO + .vxbin + resident vx_module / vx_kernel + FS variants; cbuf[8], pre-encoded OM state, pass-resident framebuffer, texture-handle table
Fallback contract
  gated (→ llvmpipe) · routed (→ on-device SW: sw_tex / sw_om / sw_raster) · silent collapse (known holes: anisotropy, mirror-clamp, alpha test, depth-bounds, dual-source)
  $MESA_VORTEX_STRICT makes a missing path a logged no-op; $VORTEXPIPE_FORCE_SW=tex|om|raster|all
Repos
  mesa_vortex (vortex_3.x) src/gallium/drivers/vortexpipe/: vp_screen.c · vp_context.c · vp_nir_to_llvm.c (~6,300 lines) · vp_compile.c · vp_launch.c · vp_raster.cpp · vp_gfx_frontend.c
Vulkan application
lavapipe (Mesa Vulkan front end): Vulkan → Gallium, NIR shaders
Gallium pipe_screen / pipe_context
vortexpipe: overridden vtable slots (vp_screen, vp_context, vp_draw_vbo …)
llvmpipe: everything not overridden (fallback + oracle)
Vortex SDK
libvortex.so · vortex2.h
$VORTEX_PATH
repos: mesa_vortex (vortex_3.x) → Vortex platform (sw/, sim/, hw/)
one-directional dependency via the install tree
Notes: Vulkan app → lavapipe (Mesa's Vulkan front end) → Gallium → vortexpipe, a thin decorator on llvmpipe that patches vtable slots in place and saves the originals; the device is reached beside the stack through the SDK. Conformance model: "inherit and accelerate" — lavapipe is both fallback and oracle. Every call either runs on Vortex, is routed to an on-device software fallback, or is gated back to llvmpipe; a strict env var turns a missing path into a logged no-op so silent non-conformance never hides.

## Slide 15: Build Configuration: TOML Single Source of Truth
Two sources
  VX_config.toml: ~230 VX_CFG_* knobs (RTL + sims)
  VX_types.toml: VX_CSR_*, VX_DCR_*, VX_ISA_*, VX_MEM_* (HW + SW)
Generator: ci/gen_config.py
  unresolved header → build/hw/VX_config.vh, build/sw/VX_config.h
  resolved header → VX_types.vh / .h
  cflags mode → XCONFIGS (-D list for Makefiles)
Expressions & types
  expr: pow(2, clog2(min($VX_CFG_DCACHE_NUM_REQS, 16)))
  [[enum]] → VX_CFG_FPU_TYPE + VX_CFG_FPU_TYPE_STD companion
  booleans: -DVX_CFG_X_ENABLE / -DVX_CFG_X_DISABLE
Why
  typed scalars, cross-key expressions, decoupled SimX/runtime from hw/
  VX_CFG_ prefix resolves LLVM / Verilator macro collisions
VX_config.toml
(hardware knobs)
VX_types.toml
(ISA / ABI contract)
ci/gen_config.py (+ CONFIGS, profiles/*.json)
VX_config.vh
VX_config.h
VX_types.vh
VX_types.h
XCONFIGS
-D list
RTL
Verilator / Vivado / Yosys
SimX +
sim/common
kernel lib, tests,
runtime (types only)
Boundary checks in CI: no sw/ or tests/ file may include VX_config.h; sw/{kernel,runtime} and sim/,hw/ never include each other (shared code → sw/common).
Notes: hw/rtl/VX_config.vh is gone. VX_config.toml holds the hardware knobs (consumed by RTL and simulators only); VX_types.toml holds the ISA/ABI contract (CSR, DCR, memory map) consumed by hardware and software. ci/gen_config.py emits unresolved headers, resolved headers, and the -D list. Every knob carries the VX_CFG_ prefix. Footgun: an unknown -D is silently ignored, so -DL2_ENABLE does nothing.

## Slide 16: Simulation Vehicles
Driver | What runs | Timing | Speed | Use it for
simx | C++ TLM model (sim/simx), MT, functional mode | cycle-level, RTL twin | fastest; 132-core profiles | architecture studies, software bring-up, CTS, oracle for parity
rtlsim | Verilator 5.028 of hw/rtl (no AFU) | cycle-exact RTL | sgemm -n32 ≈ 1.2 s | RTL development, perf_gate goldens, VCD/SAIF
xrtsim / opaesim / avedsim | Verilator of RTL + AFU shell + CP | cycle-exact incl. AFU | slower | driver and shell integration, "RTL coverage path is xrt"
gem5 | VortexGPGPU SimObject + x86-64 / AArch64 host, CP over PIO | host + device | nightly tier | host–device interaction, OS-level studies
sst | vortex.VortexGPGPU element, memory mirrored to memHierarchy | SimX clocked by SST | needs OpenMPI | system / memory-hierarchy studies
firesim | RTL on U55C, FASED DRAM, host-stepped | reproducible target cycles | sgemm -n32 ≈ 8 ms (~153× rtlsim) | long runs with RTL fidelity, memory-system sweeps
xrt / opae / aved | real AFU on Alveo / Arria-Stratix / V80 | silicon | real time | demos, timing closure, power (SAIF)
./ci/blackbox.sh --driver=simx --app=sgemm --args="-n128" --cores=4 --l2cache --perf=7
VORTEX_DRIVER=rtlsim ./tests/regression/vecadd/vecadd -n1024 # same binary, any backend
Notes: Pick by what you need to learn. simx is the C++ cycle model and the oracle for the RTL — fastest for architecture studies, scales to the 132-core h100 profile. rtlsim is Verilator on the RTL. gem5 puts a simulated host CPU in front of the command processor over real MMIO; SST mirrors memory traffic into memHierarchy for system studies. FireSim runs the RTL on an FPGA with a decoupled DRAM timing model for reproducible cycle counts at 150× rtlsim speed; the xrt/opae/aved backends run the real AFU on a card. All are selected by VORTEX_DRIVER or blackbox --driver and run the same software.

## Slide 17: SimX as the RTL Oracle: model_parity
What parity means
  SimX is the RTL's timing model, not a second ISA simulator: same pipeline modules, same cache banks, same CP model
Cases
  ci/testcases/core.yaml + per-extension catalogs (dxa, tensor_*, graphics_parity, amo…); tier full
  LR/SC apps cannot be parity cases (SimX reservations are per hart, RTL uses bounded stations)
v3 parity fixes
  cache flush fans out to i/d/t/r/o caches like VX_dcr_flush (was dcache-only)
  DXA LMEM writes counted per banked row beat — lmem_writes matches rtlsim exactly
  SimX L1 per core vs RTL per socket noted as a known gap for VM
Oracle debugging recipe
  mirror the RTL block in SimX → matching CSV trace dumps → diff → first divergence is the bug
  never widen a tolerance; fix the model or file a known_issue:
catalog case
check: model_parity
app · args · configs
simx run → PERF: instrs, cycles
rtlsim run → PERF: instrs, cycles
instrs equal?
|Δcycles| ≤ tolerance (5%)?
PARITY: line → PASS / FAIL
known_issue → xfail / XPASS
Notes: A catalog case marked check: model_parity runs the same app, args and configs on simx and rtlsim and asserts identical retired-instruction counts — a mismatch is functional divergence, not timing — and a cycle gap within the case tolerance, 5% by default. Known gaps carry an explicit known_issue reason. Debugging with the oracle: mirror the RTL structure in SimX, dump matching CSV traces from both, diff to the first divergence. v3 specifically added SimX cache-flush parity and DXA LMEM write counting to match rtlsim exactly.

## Slide 18: Perfetto: Timeline Analysis of Traces
What the exporter emits
  async slice per instruction (UUID-keyed, first stage → commit) on …: warpN
  instant stage markers schedule · decode · dispatch · execute · commit with uuid, wid, PC, tmask, ex, op, rd / rs1 / rs2 / rs3, sop / eop
  warp-state counters active · stalled · active_threads on …: warpN state
  cache / memory instants dcache:miss, l2:hit, mem:req with addr, tag; raw unmapped instants
Workflows
  long slice → copy uuid → search cache events (UUID correlation, best effort)
  active low = underutilized · stalled high = latency-bound · active_threads low = divergence
  RTL tmask normalized to SimX convention (bit 0 = thread 0)
Tips
  export a cycle window for huge logs; .json.gz recommended; --parent-flow draws parent → uop arrows when parent=#<uuid> is present
  trace at --debug=3 on either driver; v3 trace export lives in ci/perfetto.py, guide in docs/perfetto_analysis.md
Perfetto UI — Vortex GPU 1 (mock-up)
cluster0-socket0-core0: warp0
warp0 state
warp1
dcache
l2
mem
lw #a1
add
fmadd
lw #b7
bar
schedule · decode · dispatch · execute · commit (uuid, wid, PC, tmask, ex, op, rd/rs)
active / stalled / active_threads counters
lw
mul
sw
lw #c2
dcache:miss #a1
dcache:miss #b7
hit
l2:hit addr=0x8001…
l2:miss
mem:req tag=0x2a
python3 ci/perfetto.py run_simx.log -t simx -c -o vortex.perfetto.json.gz
python3 ci/perfetto.py run_rtlsim.log -t rtlsim -c --cycle-min 10000 --cycle-max 20000 -o window.json.gz
--freq-mhz 300 | --cycle-ns 3.3 --values none|dest|all --parent-flow --no-vxdrv-start
→ open ui.perfetto.dev (or the VS Code extension) and drag the .json.gz in
Notes: ci/perfetto.py converts a SimX or RTL log into Chrome Trace JSON, auto-detecting the flavour, and Perfetto renders it. One process "Vortex GPU 1" with tracks per core: a warp track with an async slice per instruction from its first stage to commit and instant markers for schedule, decode, dispatch, execute and commit carrying uuid, warp, PC, thread mask, unit, opcode and registers; a warp-state track with active, stalled and active_threads counters; and cache/memory tracks with instants such as dcache:miss, l2:hit, mem:req with address and tag. Export a cycle window for big logs; UUID correlation links an instruction to its memory traffic.

## Slide 19: CI: Tests as Data
Categories (35)
  core · cache · amo · rvc · vm · tensor{,_sp,_wg,_mx} · dxa · graphics{,_parity} · raytracing · mufu · opencl · hip · vulkan · gem5 · sst · mpi · dtm · cupbop · riscv · runtime · kernel · unittest · synthesis · fpga_gate · asic_gate · stress · scope · debug · config1/2 · zfhmin
Rules
  serial within a cell (Verilator builds raced under -n auto) · known_issue: → xfail / XPASS · every knob carries VX_CFG_
  xlen is the outer dimension (build32/ vs build64/); needs: mpi | sst | gem5 → full setup profile
ci/testcases/<category>.yaml
648 cases · 35 categories
axes: category · driver · xlen · configs · shape · tier · needs · touches
ci/testcase.py planner
lint · matrix · drivers · select
ci/conftest.py + test_runner.py
(pytest, --strict-markers)
GitHub matrix JSON
→ one job per cell
local: pytest ci -m "…"
./ci/regression.sh --test …
via:
blackbox (default)
make-run
script
VX_XLEN=32 pytest ci -m "cache and simx and smoke" --strict-markers
pytest ci --collect-only # what would run
./ci/regression.sh --all | --test tensor | --test "tensor and simx"
./ci/regression.sh --run dtm|sst|gem5|cupbop # host flows
ci.yml event | drivers × tiers
push | simx · smoke
pull_request | simx + rtlsim · smoke + full
Monday schedule | all
escalations | RTL/DPI/sim/TOML diff adds rtlsim; indeterminate diff → all drivers; AFU paths force xrt + opae
jobs | plan → setup → build (per XLEN) → tests (1 per cell) → complete
Notes: The YAML catalog under ci/testcases is the single source of truth for local and CI runs: 648 cases in 35 categories with eight axes — category, driver, xlen, configs, shape, tier, needs, touches — run by pytest with drivers as markers. It replaced about 1,400 lines of bash with hard-coded invocations. A planner turns the catalog into a GitHub matrix; the same catalog drives pytest locally. known_issue entries xfail and XPASS when fixed. Every config knob must carry the VX_CFG_ prefix because an unknown -D is silently ignored.

## Slide 20: Four Regression Gates
Shared machinery (ci/synth_gate.py)
  catalog, config_hash, thresholds, known_issue, resumable sessions (--resume), longest-first 2-up scheduling, RTL-elaboration watch (fails a config typo in minutes)
  DUTs declared once per flow in hw/syn/{xilinx,yosys}/dut/catalog.mk; make -C hw/syn/yosys/dut om and the gate run the same thing
  verdicts PASS · REGRESSION · IMPROVED · STALE · FAIL · KNOWN-ISSUE · XPASS · RECORDED
Baseline groups
  perf: core, dxa, graphics, raytracing, tensor, tensor_sp, tensor_wg, tensor_mx · synthesis: core (cache, core, top), tensor (tcu, tensor), graphics (raster, tex, om, rtu, gfx), dxa, mufu, vm
Why
  cycle regressions surface at the change that caused them; improvements fail too so gains are locked in; never widen a tolerance
  hosted 16 GB runner bounds asic_gate: top, gfx, tensor, vm are FPGA-only; core and tex at reduced width
Three flow bugs the ASIC gate caught
  report_worst_slack (signed) instead of clamped report_wns · configure copies every *.mk · override CONFIGS += (a command-line CONFIGS silently dropped -DSYNTHESIS -DASIC -DYOSYS → 1.08 M cells of FF-inferred RAM)
model_parity
simx ↔ rtlsim, same case
instrs exact · cycles ≤ 5% (per-case)
tier full · PARITY: line
perf_gate
rtlsim ↔ ci/baselines/perf/*.json
instrs exact · cycles ±2% two-sided · config_hash
update: pytest ci -m perf_gate --update-baselines
fpga_gate
Vivado synth + P&R, 9 DUTs @ target clock
Fmax, LUT ±5%; records WNS, FF, LUTRAM, BRAM, URAM, DSP, 10 worst paths
self-hosted runner · fpga_gate.yml via host cron
asic_gate
sv2v → Yosys → ABC → OpenSTA, ASAP7 RVT TT
Fmax vs target, cell area ±5%; records WNS/TNS, seq + SRAM area, cells, power
hosted, nightly, one job per DUT (1–2 h each)
Notes: model_parity and perf_gate protect behaviour and cycles; fpga_gate and asic_gate protect what synthesis costs. perf_gate runs on rtlsim against goldens in ci/baselines/perf: instructions must match exactly, cycles within ±2%, a config hash invalidates a stale golden, and an improvement beyond 2% also fails until a human locks it in — the goldens always state the real number. fpga_gate puts nine DUTs through Vivado synthesis and place-and-route on a self-hosted runner; asic_gate runs sv2v → Yosys → ABC → OpenSTA on ASAP7, nightly, one hosted job per DUT. Both share ci/synth_gate.py.

## Slide 21: Writing a Native Vortex Program
Layout
  tests/regression/<name>/{kernel.cpp, main.cpp, common.h, Makefile}; Makefile includes ../common.mk
  ../configure after adding the folder; make -C tests/regression/<name>
Run
  ./ci/blackbox.sh --driver=simx --app=<name> --args="-n1024"
  --driver=rtlsim --debug=3 --vcd for traces and waveforms; --perf=<class> for counters
CONFIGS discipline
  app and driver must agree: CONFIGS="-DVX_CFG_NUM_THREADS=8 -DVX_CFG_EXT_TCU_ENABLE" make -C tests/regression/sgemm_tcu
  never hard-code -DVX_CFG_* in a Makefile — VX_config.toml is the single source of truth
Examples to copy
  vecadd · sgemm · sgemm_tcu · sgemm2_dxa_mcast · cta_cluster · multikernel · amo · raycast · gfx_draw3d
// kernel.cpp
#include <vx_spawn2.h>
#include "common.h" // kernel_arg_t
__kernel void kernel_body(kernel_arg_t *arg) {
uint32_t i = blockIdx.x * blockDim.x + threadIdx.x;
auto a = (float*)arg->a_addr, b = (float*)arg->b_addr;
auto c = (float*)arg->c_addr;
if (i < arg->n) c[i] = a[i] * b[i];
}
// main.cpp
vx_dev_open(0, &dev); vx_queue_create(dev, &q);
vx_mem_alloc(dev, bytes, VX_MEM_READ, &bufA); …
vx_module_load_file(dev, "kernel.vxbin", &mod);
vx_module_get_kernel(mod, "kernel_body", &kern);
vx_launch_info_t li{kern, &args, sizeof(args), 1, {n/B}, {B}};
vx_enqueue_memcpy_htod(q, bufA, hA, bytes, 0, nullptr);
vx_enqueue_launch(q, &li, &ev); vx_event_wait_value(ev, 1);
Notes: For architecture work the native path is the shortest: a kernel.cpp using vx_spawn2.h, a main.cpp using vortex2.h, and a Makefile that includes tests/regression/common.mk. The test is a folder under tests/regression and runs through blackbox.sh on any driver. CONFIGS must match between app and driver — rebuild the app when changing NUM_THREADS or enabling an extension.

## Slide 22: Debugging and Tooling
AGENTS.md rules that matter here
  run tests from build/; CONFIGS must match app and driver; no --rebuild
  RTL verification path is xrt, not rtlsim (rtlsim bypasses the AFU)
  root-cause bugs; no legacy fallbacks; label unavoidable patches
Where things log
  tests/regression/logs/ (run_parallel.sh) · blackbox.<driver>.cache remembers the last config
Roofline
  ci/roofline.py --app=… --flops=… --plot
Need | Tool
instruction trace | --debug=1..3 (rtlsim / simx) → run.log; --no-vxdrv-start for RTL logs without the driver marker
waveforms | --vcd [--vcd_file=…] independent of --debug
activity / power | --saif [--saif_file=…] → Synopsys / Vivado power (SAIF_INST = DUT path)
counters | --perf=<class> (MEM 7, RASTER 12, TEX 13, OM 14, RTU 15, DXA 16, …)
timeline | ci/perfetto.py run.log -t simx¦rtlsim -c -o trace.json.gz → Perfetto UI
printf | vx_printf in kernels → host console via the runtime
ISA tests | riscv-tests built per XLEN on demand; ELF loader + HTIF tohost monitor (run-{simx,rtlsim}-{32,64}[c])
model diff | SimX-as-oracle: matching CSV trace dumps from SimX and RTL, diff → first divergence
bisection | tinygpu profile (1 core, 2×2, no caches/LMEM) + sgemm to separate infra from core bugs
Notes: Instruction traces at three debug levels, VCD waveforms, SAIF activity for power, perf-counter classes, Perfetto timelines (session 7), vx_printf from kernels, HTIF/ELF loading for riscv-tests, and SimX-as-oracle differential debugging against the RTL. The regression script's configs are the canonical tested set; tinygpu isolates infrastructure bugs from core bugs.

## Slide 23: Takeaways
Compiler
VOLT (LLVM 20 + Vortex RISC-V backend) sits under OpenCL, HIP, CUDA and Vulkan — covered in detail in the next talk
Kernel ABI
vx_spawn2.h __kernel (no callee-saved spills), CTA CSRs, split barriers, vx_tensor.h / vx_dxa.h; VXSYMTAB multi-kernel .vxbin
Runtime
vortex2.h: 6 handles, queues + timeline events, modules/kernels, UVA args over a host-resident CP ring; stub + VORTEX_DRIVER; SDK + pkg-config
Front ends
PoCL 7.0 (ICD-only, async worker, images on TEX, Rodinia), chipStar HIP on rv32 + rv64, vortexpipe Vulkan from NIR
Config / sim
VX_config.toml + VX_types.toml single source; simx (RTL twin), rtlsim, gem5, SST, FireSim selected by VORTEX_DRIVER
CI
648 catalogued cases, pytest + GitHub matrix; model_parity, perf_gate ±2%, fpga_gate / asic_gate ±5%; Perfetto timelines from any log

## Slide 24
Thank You!
https://github.com/vortexgpgpu/vortex · pocl · chipStar · mesa
docs/designs: opencl_on_vortex · hip_on_vortex_chipstar · vortex_runtime_api · simx_simulator_architecture · continuous_integration
docs: perfetto_analysis.md · simulation.md · testing.md · AGENTS.md